## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 02

## Slide 2
If a tree falls in a forest and no one is around to hear it, does it make a sound?

## Slide 3
How certain is our world?

## Slide 4
Immanuel Kant: We can never know things in themselves (noumena); we only know things as they appear to us (phenomena).
Arthur Schopenhauer: The world is my representation
Niels Bohr: Physics is not about how the world is, it is about what we can say about the world
Albert Einstein: Reality is independent of the observer, but our theories try to approximate it
Nikolai Bukharin: Matter exists independently of consciousness, and the task of science is to understand its laws.

## Slide 5
Observer
Objective Reality
Experiment
Measurement
Theory
Understanding (κατανόηση) of physical laws
Effect (επίδραση) on physical laws

## Slide 6
Συσκευές και Αισθητήρες

## Slide 7
IoT Recap (1)
IoT is a network of physical objects (“things”) embedded with sensors, actuators, processors and communication interfaces that collect, exchange and act upon data to monitor, control, or optimize environments or processes, often without direct human intervention.
An IoT device is a standalone or networked system that integrates sensors, actuators, and a processor to perceive its environment, process the data and take action or communicate results as part of an IoT ecosystem.
A sensor is a hardware component that detects and measures a specific physical, chemical, or biological property from the environment and converts it into a readable electrical signal for processing.
An actuator is a hardware component that converts electrical signals from a processor into a physical action or effect, such as movement, light, heat, or sound, to influence the environment.
A processor in an IoT system is a computing unit, such as a microcontroller (MCU), microprocessor (MPU), or System-on-Chip (SoC), that executes instructions, processes data from sensors, makes decisions and controls actuators or communication modules within the IoT device.

## Slide 8
IoT Recap (2)

## Slide 9
Sensors (1): Environmental & Physical
Sensor Type | Example | Measurement | Output | Typical Use Case | Sensor Type
Temperature | DHT22, TMP36 | Temperature (°C/°F) | Analog / Digital (I²C) | Weather stations, climate control | Temperature
Humidity | DHT22, SHT31 | Relative humidity (%) | Digital (I²C/SPI) | Smart home, agriculture | Humidity
Pressure / Altitude | BMP280, BME280 | Barometric pressure (Pa), altitude (m) | Digital (I²C/SPI) | Drones, weather monitoring, IoT altimeters | Pressure / Altitude
Light / Luminance | BH1750, TSL2561 | Light intensity (lux) | Digital (I²C) | Smart lighting, energy management | Light / Luminance
Gas / Air Quality | MQ-2, CCS811 | CO, CO₂, LPG, air quality | Analog/Digital | Air quality monitoring, control | Gas / Air Quality
Proximity / Distance | Ultrasonic HC-SR04, VL53L0X | Distance to object (cm) | Digital | Obstacle detection, robotics | Proximity / Distance
DHT22
TMP36
BMP280

## Slide 10
Sensors (2): Motion, Position & Imaging
Sensor Type | Example | Measurement | Output | Typical Use Case | Sensor Type
Accelerometer | MPU6050, ADXL345 | Linear acceleration (X/Y/Z) | Digital (I²C/SPI) | Robotics, fitness trackers, motion detection | Accelerometer
Gyroscope | MPU6050, L3G4200D | Angular velocity (deg/s) | Digital | Drones, VR controllers, robotics | Gyroscope
Magnetometer | HMC5883L | Magnetic field / compass | Digital (I²C) | Navigation, robotics | Magnetometer
IMU (Inertial Measurement Unit) | MPU6050/9250 | Acceleration + Rotation + Orientation | Digital | Robotics, drones, motion tracking | IMU (Inertial Measurement Unit)
Camera / Image Sensor | Raspberry Pi Camera, OV7670 | Visual data | Digital | Surveillance, computer vision, smart homes | Camera / Image Sensor
PIR Motion Sensor | HC-SR501 | Human/animal motion detection | Digital | Security, lighting automation | PIR Motion Sensor
MPU6050
L3G4200D
HC-SR501

## Slide 11
Sensors (3): Chemical, Biological & Specialized
Sensor Type | Example | Measurement | Output | Typical Use Case | Sensor Type
Gas / Chemical | MQ-7 (CO), MQ-135 (air quality) | Concentration of gas (ppm) | Analog / Digital | Air quality, safety monitoring | Gas / Chemical
pH / Soil Moisture | Capacitive soil sensor, pH probe | Soil moisture (%), pH | Analog / Digital | Smart agriculture | pH / Soil Moisture
Water Quality | TDS sensor, Turbidity sensor | Dissolved solids, turbidity | Analog / Digital | Aquaponics, water monitoring | Water Quality
Sound / Audio | Microphone sensor, MAX9814 | Sound amplitude | Analog / Digital | Voice assistants, noise monitoring | Sound / Audio
Vibration / Tilt | SW-420, ADXL345 | Vibrations or tilt angle | Digital / Analog | Machinery health, security | Vibration / Tilt
RFID / NFC | RC522 | Presence / identity | Digital | Access control, inventory management | RFID / NFC
MQ-7
MAX9814
RC522

## Slide 12
Actuators (1): Motion & Mechanical
Actuator Type | Example | Action | Control Method | Typical Use Case | Actuator Type
DC Motor | Generic DC motor | Rotational motion | PWM / H-bridge | Robotics, fans, conveyor belts | DC Motor
Servo Motor | SG90, MG996R | Precise angular motion | PWM | Robotics, camera pan/tilt, automation | Servo Motor
Stepper Motor | NEMA 17 | Precise step rotation | Step pulses | 3D printers, CNC machines, robotics | Stepper Motor
Solenoid | 12V linear solenoid | Linear push/pull motion | Digital ON/OFF | Door locks, valves, vending machines | Solenoid
Linear Actuator | Electric linear actuator | Extend/retract | PWM or H-bridge | Industrial automation, smart furniture | Linear Actuator
See demo: https://www.youtube.com/watch?v=WPQNad2gvEs

## Slide 13
Actuators (2): Electrical, Light & Sound
Actuator Type | Example | Action | Control Method | Typical Use Case | Actuator Type
LED / RGB LED | WS2812, standard LEDs | Light emission | GPIO / PWM / Digital | Indicators, smart lighting, displays | LED / RGB LED
Buzzer / Speaker | Piezo buzzer, DFPlayer Mini | Sound / alerts | PWM / DAC / Digital | Alarms, notifications, voice feedback | Buzzer / Speaker
Relay | 5V/12V electromagnetic relay | Switch AC/DC circuits | Digital ON/OFF | Home automation, industrial control | Relay
Solenoid Valve | Water solenoid valve | Control fluid flow | Digital / PWM | Smart irrigation, liquid control | Solenoid Valve
Heating Element | PTC, resistive heater | Generate heat | PWM / ON-OFF | Climate control, 3D printers, incubators | Heating Element
See demo: https://www.youtube.com/shorts/VxPX1zSTuP8

## Slide 14
Actuators (3): Specialized / Advanced
Actuator Type | Example | Action | Control Method | Typical Use Case | Actuator Type
Stepper/Servo with Encoder | Closed-loop servo | Precise motion feedback | PWM + Encoder | Robotics, automation, CNC | Stepper/Servo with Encoder
Vibration Motor | ERM or LRA motors | Vibration feedback | PWM / DC | Wearables, haptics, notifications | Vibration Motor
Peltier Module | TEC1-12706 | Heating/cooling | PWM / H-bridge | Temperature control, mini coolers | Peltier Module
Piezo Actuator | Piezoelectric element | Micro displacement or vibration | High-voltage pulse | Precision positioning, sensors, actuators | Piezo Actuator
Linear Piezo Motor | Piezo stack motor | High-precision linear motion | High-voltage pulse | Optical systems, micro-robotics | Linear Piezo Motor
See demo: https://www.youtube.com/shorts/xmd2YW0QwUk

## Slide 15
Processors: Arduino – Microcontroller Unit (MCU)
Type: 8-bit Microcontroller (ATmega328 / ATmega2560)
Clock Speed: 16 MHz (typical)
Memory: SRAM 2 KB / Flash 32 KB / EEPROM 1 KB
I/O Interfaces: GPIO, PWM, ADC (10-bit), UART, SPI, I²C
Power: 5V or 3.3V operation, low power (~50 mA typical)
Programming Environment: Arduino IDE, C/C++
Use Cases: Simple sensors/actuators, low-power IoT devices, prototyping, robotics
Strengths: Deterministic timing, very low power, simple to use, huge community support
Limitations: Limited processing power, no OS, limited memory

## Slide 16
Processors: ESP32 – Wi-Fi & Bluetooth MCU
Type: 32-bit Dual-core Microcontroller (Tensilica Xtensa LX6)
Clock Speed: Up to 240 MHz
Memory: SRAM 520 KB, Flash 4 MB (typical), supports external PSRAM
Connectivity: Wi-Fi 802.11 b/g/n, Bluetooth 4.2 BLE
I/O Interfaces: GPIO, ADC (12-bit), DAC, PWM, SPI, I²C, UART, Capacitive touch
Power: 3.3V operation, ultra-low-power sleep modes
Programming Environment: Arduino IDE, ESP-IDF, MicroPython
Use Cases: Smart home devices, wearable IoT, wireless sensors, edge computing
Strengths: Integrated connectivity, high processing power, versatile I/O
Limitations: More complex than Arduino, slightly higher power consumption

## Slide 17
Processors: Raspberry Pi – Microprocessor-based IoT Computer
Type: 64-bit Quad-core ARM Cortex-A53 (Raspberry Pi 3) or ARM Cortex-A72 (Pi 4)
Clock Speed: 1.2 – 1.5 GHz (Pi 3/4)
Memory: 1–8 GB LPDDR2/LPDDR4 RAM, MicroSD storage
I/O Interfaces: GPIO, SPI, I²C, UART, USB, HDMI, Ethernet, Wi-Fi, Bluetooth
Power: 5V via USB-C (Pi 4), 2.5–3 A typical
Operating System: Linux-based (Raspbian / Raspberry Pi OS)
Use Cases: Edge computing, IoT gateways, computer vision, AI prototyping, robotics
Strengths: Runs full OS, multitasking, supports high-level programming (Python, C++, Node.js)
Limitations: Higher power consumption, non-deterministic real-time behavior

## Slide 18
Processors: NVIDIA Jetson – Edge AI Processor
Type: ARM Cortex-A57 CPU + 128-core Maxwell GPU (Nano) / Volta GPU (Xavier)
Clock Speed: CPU 1.43 GHz (Nano) / 1.4 GHz (Xavier)
Memory: 4 GB LPDDR4 (Nano) / 8 GB LPDDR4 (Xavier)
I/O Interfaces: GPIO, I²C, SPI, UART, USB 3.0, Ethernet, Camera interfaces (CSI)
Operating System: Linux for Tegra, supports Docker, CUDA, TensorRT
Power: 5–10 W (Nano), 10–30 W (Xavier)
Use Cases: AI at the edge, computer vision, deep learning, autonomous robots, smart cameras
Strengths: GPU acceleration, supports ML/AI inference, edge processing capability
Limitations: Expensive, higher power, learning curve for CUDA/ML frameworks
https://developer.nvidia.com/embedded/jetson-benchmarks

## Slide 19
IoT Devices Across Verticals (1)
Vertical / Domain | IoT Device | Processor | Sensors | Actuators | Typical Use Case
Smart Home | Smart Thermostat | ESP32 / Arduino | DHT22 (Temp/Humidity), Light sensor | Relay (HVAC), RGB LED | Climate control, energy saving
 | Smart Lighting | ESP32 / Arduino | PIR motion sensor, Light sensor | LED strips, Relay | Automated lighting, occupancy-based control
 | Smart Door Lock | ESP32 / Arduino | RFID/NFC reader, Contact sensor | Solenoid, Motor | Access control, home security
Healthcare / Wearables | Fitness Tracker | ESP32 / Arduino | Accelerometer (MPU6050), Heart rate sensor | Vibration motor, LED indicator | Activity monitoring, notifications
 | Remote Patient Monitor | Raspberry Pi / ESP32 | Temperature sensor, Pulse oximeter | Buzzer / Display | Alerts, patient monitoring

## Slide 20
IoT Devices Across Verticals (2)
Vertical / Domain | IoT Device | Processor | Sensors | Actuators | Typical Use Case
Agriculture / Environment | Smart Irrigation | ESP32 / Arduino | Soil moisture, DHT22 | Solenoid valve, Pump | Watering automation, crop management
 | Weather Station | Raspberry Pi | BMP280 (Pressure), DHT22, Rain sensor | Servo for rain shield | Climate monitoring, data logging
Industrial / IIoT | Predictive Maintenance | Raspberry Pi / Jetson Nano | Vibration sensor, Temperature sensor | Alarm / Relay | Machine failure alerts
 | Smart Conveyor System | Arduino / ESP32 | Proximity sensor, Load sensor | Motor, Solenoid | Automated material handling
Smart City / Public Infrastructure | Smart Street Light | ESP32 | PIR sensor, Light sensor | LED streetlights, Relay | Energy-efficient lighting
 | Traffic Monitoring | Raspberry Pi / Jetson | Camera, Ultrasonic sensor | LED signals, Signs | Real-time traffic control

## Slide 21
Mini Demo 1 – Explore IoT
Identify the component
Try it hands-on

## Slide 22
Mini Demo 1 – Pi Architecture

## Slide 23
Mini Demo 1 - Flashing the SD Card
Steps:
Download the OS image (e.g., Raspberry Pi OS, Ubuntu IoT).
Insert SD card into your computer.
Use flashing tool (Balena Etcher, Raspberry Pi Imager, Win32DiskImager).
Select image + SD card in the tool.
Flash / Write the OS onto the SD card.
Insert SD card into device (Pi, Jetson, etc.) and boot.

## Slide 24
Mini Demo 1 – Getting Started
Steps:
1. Insert SD Card with flashed OS into the device.
2. Connect Keyboard & Mouse via USB ports.
3. Attach Display using HDMI cable.
4. Power On the device using the correct adapter.
5. Initial Boot – OS expands, basic configuration runs (language, Wi-Fi, updates).

## Slide 25
Mini Demo 1 – Connecting Raspberry Pi to Wi-Fi
Method 1: Physical Access (GUI)
Boot Pi with monitor, keyboard, and mouse.
Click on the Wi-Fi icon (top-right menu bar).
Select your network → Enter password.
Confirm connection (check IP via terminal: ifconfig or ip a)
Method 2: Terminal
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
Add new network block:
network={
ssid="YourNetworkName"
psk="YourPassword"
}
Method 3: Headless Setup (No Monitor)
On SD card, create a file wpa_supplicant.conf in the boot partition with the Wi-Fi details

## Slide 26
Mini Demo 1 – Enable SSH
Method 1: Physical Access (GUI)
Boot Pi with monitor + keyboard.
Open Raspberry Pi Configuration → Interfaces tab.
Enable SSH.
Method 2: Terminal
sudo systemctl status ssh
sudo systemctl enable ssh # Start on boot
sudo systemctl start ssh # Start now
sudo systemctl stop ssh # Stop service
sudo systemctl disable ssh # Disable on boot
hostname –I # Find the Pi IP address
Method 3: Headless Setup (No Monitor)
On the SD card (boot partition), create an empty file named: “ssh”
Method 2: Create user and pass
sudo adduser newuser
sudo usermod -aG sudo newuser
sudo systemctl enable --now ssh

## Slide 27
Mini Demo 1 – Connect via SSH
Windows Powershell
ssh pi@<raspberrypi-ip>
Linux Terminal
ssh pi@<raspberrypi-ip>
Android
JuiceSSH, Termius, ConnectBot
iOS
Termius, Shelly
What happens if your Pi is on 192.168.1.20 but your laptop is on 10.0.0.15?

## Slide 28
Mini Demo 1 – Sub-networking
SSH works if client and Pi are on the same subnet (e.g. 192.168.1.x).
If they’re on different networks (e.g. laptop on 192.168.1.x, Pi on 10.0.0.x), the devices cannot reach each other directly.
This is because routers/NAT separate broadcast domains and block local IP discovery.
Solution requires:
  Port forwarding (access across WAN)
  VPN / Tunneling
  or IoT gateways (future topic).

## Slide 29
Mini Demo 2 – Arduino Coding via WokWi
https://wokwi.com/
Example: Timely control an LED
Tools: Arduino Uno, LED, resistor.
Components:
  Arduino Uno
  LED (red)
  220 Ω resistor
  Breadboard & jumper wires

## Slide 30
Mini Demo 2 – Wiring Diagram
{
"version": 1,
"author": "Class Demo",
"editor": "wokwi",
"parts": [
{ "type": "wokwi-arduino-uno", "id": "uno", "top": 0, "left": 0 },
{ "type": "wokwi-led", "id": "led1", "top": -50, "left": 80, "attrs": { "color": "red" } },
{ "type": "wokwi-resistor", "id": "r1", "top": -65, "left": 180, "attrs": { "value": "220" } }
],
"connections": [
["led1:A", "r1:1", "green", ["v0"]],
["r1:2", "uno:13", "green", ["v0"]],
["led1:C", "uno:GND.1", "green", ["v0"]]
],
"dependencies": {}
}
GUI
  LED anode (long leg) → resistor → Pin 13
  LED cathode (short leg) → GND
  Resistor limits current to protect the LED
JSON schema

## Slide 31
Mini Demo 2 – Code Logic
const int ledPin = 13;
void setup() {
pinMode(ledPin, OUTPUT);
}
void loop() {
digitalWrite(ledPin, HIGH);
delay(500);
digitalWrite(ledPin, LOW);
delay(500);
}
ledPin defines the digital pin connected to the LED
pinMode(ledPin, OUTPUT) sets the pin as an output
digitalWrite(ledPin, HIGH) turns the LED on
digitalWrite(ledPin, LOW) turns the LED off
delay(500) pauses the program for 500 milliseconds
The loop() function repeats endlessly, causing the LED to blink
setup() runs once, loop() runs forever
Change delay() to make the LED blink faster or slower

## Slide 32
References
Baller, Stephan Patrick, et al. "DeepEdgeBench: Benchmarking deep neural networks on edge devices." 2021 IEEE International Conference on Cloud Engineering (IC2E). IEEE, 2021.
Do, Xuan Phu, and Seung Bok Choi. "A state-of-the-art on smart materials actuators over the last decade: Control aspects for diverse applications." Smart Materials and Structures 31.5 (2022): 053001.
Swartz, Robert J., ed. Perceiving, sensing, and knowing: a book of readings from twentieth-century sources in the philosophy of perception. Vol. 4. Univ of California Press, 2023.
Javaid, Mohd, et al. "Sensors for daily life: A review." Sensors International 2 (2021): 100121.
Petrović, Nenad, Samir Koničanin, and Suad Suljović. "ChatGPT in IoT systems: Arduino case studies." 2023 IEEE 33rd International Conference on Microelectronics (MIEL). IEEE, 2023.
https://projects.raspberrypi.org/en/projects/raspberry-pi-getting-started
https://www.arduino.cc/en/Tutorial/HomePage/
Karvinen, Kimmo, and Tero Karvinen. Getting started with sensors: Measure the world with electronics, arduino, and raspberry pi. Maker Media, Inc., 2014.
Sarvajcz, Kornel, Laszlo Ari, and Jozsef Menyhart. "Ai on the road: nvidia jetson nano-powered computer vision-based system for real-time pedestrian and priority sign detection." Applied Sciences 14.4 (2024): 1440.
https://github.com/PacktPublishing/Jetson-Nano-Starter-to-Pro---A-Computer-Vision-Course

## Slide 33
Questions/Discussion
?