## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 03

## Slide 2
If a tree falls in a forest and no one is around to hear it, does it make a sound?
Protocol

## Slide 6
If a tree falls in a forest and no one is around to hear it, does it make a sound?
Communication Protocol

## Slide 9
Πρωτόκολλα και Τεχνολογίες Διαχείρισης Συσκευών IoT

## Slide 10
Why IoT Devices Need Protocols
Devices have limited power, processing and bandwidth
Reliable communication is essential for sensor data, commands and updates
Protocols provide standardized rules for messaging
Handle disconnections, message loss and scale

## Slide 11
Protocol Taxonomy
IoT Protocols
Network/Transport Protocols
App/Data Protocols
handle how data is transmitted over networks
define format and semantics of messages

## Slide 12
Protocol Types
Category | Protocol | Basic Functionality | Pros | Cons
Network/Transport | HTTP/HTTPS | Standard web communication | Widely supported, easy to debug | Heavy for low-power devices
 | LoRaWAN | Long-range, low-power | Very low energy, wide coverage | Low data rate, latency
 | Bluetooth / BLE | Short-range, low-power | Low energy, easy pairing | Short range, interference
 | Zigbee | Short-range mesh network | Low power, reliable mesh | Limited bandwidth, vendor-specific
Data/Application | MQTT | Pub/sub messaging via broker | Lightweight, scalable, QoS support | Needs broker, not real-time
 | CoAP | REST-like, for constrained devices | Lightweight, low overhead | Limited tooling, smaller ecosystem
 | AMQP | Enterprise messaging | Reliable, transactional | Heavy for small devices
 | XMPP | Extensible messaging & presence | Standardized, real-time | Complex for constrained devices
 | DDS | Real-time data distribution | High performance, deterministic | Heavy, complex setup

## Slide 13
Messaging Patterns
Pattern / Aspect | Description
Request/Response | Synchronous, client asks and waits for server; tight coupling, simple, good for commands or configs.
Pub/Sub/Topics | Asynchronous, decoupled, scalable; one-to-many or many-to-many; ideal for sensor broadcasts.
Event-Drive | Devices notify subscribers when specific events happen; similar to pub/sub but often more reactive.
Message Queue (MQ / FIFO) | Messages are stored in a queue until processed; ensures order and reliability; good for buffered workloads.
Streaming/Continuous Data | Continuous flow of data - ideal for telemetry, logs, or real-time analytics.
Multicast/Broadcast | One message sent to multiple recipients simultaneously; efficient for local networks.
Command & Control & Actuation | Direct commands to devices for industrial IoT.

## Slide 14
MQTT Overview
MQTT (Message Queuing Telemetry Transport) is a lightweight, publish/subscribe messaging protocol designed for IoT and constrained devices.
Lightweight and efficient: MQTT implementation on the IoT device requires minimal resources, so it can even be used on small microcontrollers.
Scalable: MQTT implementation requires a minimal amount of code that consumes very little power in operations. The protocol also has built-in features to support communication with a large number of IoT devices.
Reliable: Many IoT devices connect over unreliable cellular networks with low bandwidth and high latency. MQTT has built-in features that reduce the time the IoT device takes to reconnect with the cloud. It also defines three different quality-of-service levels to ensure reliability for IoT use cases— at most once (0), at least once (1), and exactly once (2).
Secure: MQTT makes it easy for developers to encrypt messages and authenticate devices and users using modern authentication protocols, such as OAuth, TLS1.3, Customer Managed Certificates, and more.
Well-supported: Several languages like Python have extensive support for MQTT protocol implementation. Hence, developers can quickly implement it with minimal coding in any type of application.
https://aws.amazon.com/what-is/mqtt/

## Slide 15
MQTT – How it works (1)
1. Devices publish messages to topics on the broker
  Each message is sent to a specific topic (like a channel or label).
  Publishers don’t need to know who will read it, simplifying device logic.
  Example: /home/livingroom/temperature → any subscriber listening to that topic receives updates.
2. Devices subscribe to topics they care about
  Subscribers express interest in certain topics; they automatically receive messages published there.
  Decouples devices: multiple subscribers can receive the same data without the publisher managing each connection.
  Example: Dashboard, mobile app, or another sensor subscribing to /temperature.

## Slide 16
MQTT – How it works (2)
3. Broker ensures delivery, retries and QoS
  The broker acts as a central coordinator, managing:
    Message delivery (to all active subscribers)
    Retries for QoS levels 1 and 2
    Message retention if needed (so late subscribers get the last value)
  This reliability mechanism is critical for intermittent connections common in IoT networks.
4. Decouples senders and receivers
  Publishers and subscribers never need to know each other’s identity or IP address.
  Makes IoT systems more scalable and flexible: devices can join/leave dynamically without breaking communication.
  Supports loosely coupled architectures, ideal for distributed sensor networks.

## Slide 17
MQTT – Smart Home

## Slide 18
MQTT – Connected Vehicles

## Slide 19
MQTT – IIoT

## Slide 20
MQTT Demo 1: Setup Broker
Laptop
MQTT publisher
MQTT broker
WiFi
Smartphones
MQTT listener
Install Mosquitto (https://mosquitto.org/download/)
Fix config file C:\Program Files\mosquito\mosquitto.conf
  allow_anonymous true
  listener 1883
  protocol mqtt
Load service
  Open Services (Win + R → services.msc)
  Find Mosquitto Broker → right-click → Start
Disable firewall
PS C:\Program Files\mosquitto> netstat -an | findstr 1883
TCP 0.0.0.0:1883 0.0.0.0:0 LISTENING
TCP [::]:1883 [::]:0 LISTENING
TCP [::1]:1883 [::1]:49734 TIME_WAIT
TCP [::1]:1883 [::1]:54432 TIME_WAIT
TCP [::1]:1883 [::1]:54433 TIME_WAIT
TCP [::1]:1883 [::1]:54434 TIME_WAIT
TCP [::1]:1883 [::1]:54435 TIME_WAIT

## Slide 21
MQTT Demo 1: Setup Publisher
Laptop
MQTT publisher
MQTT broker
WiFi
Smartphones
MQTT listener
import time import random import paho.mqtt.client as mqtt # ----------------------------- # Fixed Parameters (Change here) # ----------------------------- BROKER = "192.168.1.22" # MQTT broker IP (PC LAN) PORT = 1883 # MQTT broker port TOPIC = "test/topic" # MQTT topic QOS = 1 # QoS level (0, 1, 2) INTERVAL = 2.0 # Seconds between messages CLIENT_ID = "TemperaturePublisher" # Unique client ID # ----------------------------- # MQTT Setup # ----------------------------- client = mqtt.Client(CLIENT_ID) client.connect(BROKER, PORT) print(f"Connected to MQTT broker {BROKER}:{PORT}, publishing to topic '{TOPIC}' with QoS={QOS}") # ----------------------------- # Continuous Publish Loop # ----------------------------- try: while True: # Simulate temperature sensor temperature = round(random.uniform(20.0, 30.0), 2) payload = f"{{'temperature': {temperature}}}" # Publish message client.publish(TOPIC, payload, qos=QOS) print(f"Published: {payload}") # Wait for next interval time.sleep(INTERVAL) except KeyboardInterrupt: print("Stopping publisher...") client.disconnect()

## Slide 22
MQTT Demo 1: Setup Listeners
Laptop
MQTT publisher
MQTT broker
WiFi
Smartphones
MQTT listener
Install MQTT client
  https://play.google.com/store/apps/details?id=com.shan.livemq&pcampaignid=web_share
Connect to broker
  Server IP= 10.193.92.224
  MQTT 3.1.1
  No Pass
  No SSL
Subscribe to topic: test/topic
Receive messages!!

## Slide 23
MQTT Demo 2: Publish Votes
broker = "192.168.1.22"
port = 1883 vote_topic = "/class/vote“
Vote A or B for the following MIT ethical scenarios and see the results
https://www.moralmachine.net/

## Slide 24
MQTT Demo 2: Scenario 01
A
B

## Slide 25
MQTT Demo 2: Scenario 02
A
B

## Slide 26
MQTT Demo 2: Scenario 03
A
B

## Slide 27
MQTT Demo 2: Scenario 04
A
B

## Slide 28
MQTT Challenges
Group Discussion: MQTT challenges on large-scale IoT environments

## Slide 29
MQTT Challenges
Network reliability
  Disconnection?
  MQTT relies on broker and network connectivity; QoS helps but cannot fully replace network failures.
Scalability limits
  Multiple devices publishing simultaneously → how does the broker handle high message rates?
  Potential bottleneck if broker isn’t robust.
Resource constraints
  Smartphones are relatively powerful; real IoT sensors may have limited memory, CPU, battery.
  How does MQTT perform on microcontrollers?
Message ordering & timing
  Messages may arrive out of order (especially QoS 0 or with multiple topics).
  Important for real-time systems.
Security concerns
  Our demo likely ran without authentication or encryption.
  In production: use TLS/DTLS, username/password, client certificates.
Topic management
  With many devices and topics, keeping a clean and consistent topic hierarchy can be challenging.
Broker dependency
  Centralized broker → single point of failure if not highly available.
  How could you make it redundant or distributed?

## Slide 30
Device Management in IoT
Monitoring: track device status, health, and connectivity
Firmware updates: deploy patches or new features remotely
Configuration: adjust device settings without physical access
Security: revoke access, rotate keys, monitor for anomalies
Essential for scaling IoT networks with hundreds or thousands of devices

## Slide 31
Device Management Protocols
Protocol | Basic Functionality | Pros | Cons
OMA LwM2M | Device registration, configuration, monitoring, firmware updates | Lightweight, designed for constrained devices, secure (DTLS), standard for IoT device management | Requires server infrastructure, less widespread tooling than older protocols
OMA DM | Device provisioning and configuration (originally for mobile phones) | Mature, widely deployed in mobile ecosystem | Heavy for constrained IoT devices, uses verbose XML, slower than LwM2M
TR-069 / CWMP | Remote device management for broadband CPE | Standardized for ISPs, supports provisioning, firmware updates | Mostly used for gateways/routers, heavier than LwM2M, not ideal for small IoT sensors

## Slide 32
Introduction to LwM2M
Lightweight M2M (LwM2M) protocol for device management and telemetry
Designed for constrained IoT devices (low power, low bandwidth)
Supports device registration, configuration, firmware updates, monitoring
Operates over CoAP (UDP-based) and optionally DTLS for security
LwM2M Client: The client on the IoT device executes commands, collects data, and manages resources.
LwM2M Server: The server is the central entity that communicates with the client. It issues commands, receives data, and performs management tasks like firmware updates and configuration changes.
LwM2M Objects: Objects are logical groupings of resources on the client device. Each object represents a specific functionality or data type, such as device information, location data, or sensor readings.
https://www.hashstudioz.com/blog/lwm2m-protocol-in-iot-what-is-it-and-why-is-it-important/

## Slide 33
LwM2M Device Registration
Devices register with a management server when powered on
Server maintains a device registry with metadata: type, capabilities, status
Supports bootstrap for automatic provisioning (the server can initiate a bootstrap process to configure the client with necessary settings and security credentials).

## Slide 34
LwM2M Remote Configuration & Monitoring
Server can push new configuration (thresholds, reporting intervals)
Devices can report telemetry periodically or on events
Real-time monitoring enables alerts on faults or anomalies

## Slide 35
LwM2M Firmware Updates
Devices can receive OTA (Over-the-Air) updates securely
Updates can be scheduled or triggered by server
Ensures devices are up-to-date without physical access

## Slide 36
IoT Platforms based on LwM2M
Cloud / Platform | Protocol Support | Major Use-Cases / Examples | Notes
AWS IoT Core / AWS IoT Device Management | LwM2M (via SDK), MQTT | Smart home devices, industrial sensors, telemetry dashboards | Device registry, OTA updates, monitoring, rules engine
Azure IoT Hub / IoT Central | LwM2M (via SDK), MQTT, AMQP | Connected vehicles, smart buildings, factory sensors | Device provisioning, configuration, remote updates, cloud dashboards
ThingsBoard (Open Source) | LwM2M, MQTT | Smart agriculture, energy metering, home automation | Device registry, telemetry collection, dashboards, rule engine
Mainflux (Open Source) | LwM2M, MQTT | Industrial sensors, IoT gateways | Device management, telemetry, multitenant support
OpenRemote (Open Source) | LwM2M, MQTT, HTTP | Smart building automation, energy management | Focus on integration, visualization, automation workflows

## Slide 37
A look into ThingsBoard
Protocol Support: LwM2M, MQTT, HTTP
Use-Cases:
  Smart agriculture (soil sensors, irrigation)
  Energy metering (smart grids, building energy management)
  Home automation (smart plugs, temperature sensors)
Device Management Features:
  Device registry & metadata management
  Remote configuration and OTA firmware updates
  Telemetry collection and monitoring
Visualization & Analytics:
  Custom dashboards for real-time data
  Rule engine for event-driven actions
Open-Source Advantages:
  Free to use and extend
  Active community support
https://thingsboard.io/docs/getting-started-guides/what-is-thingsboard/

## Slide 38
System Design: An IoT optimization game
Sensor | Importance (1–10) | Battery Cost per Report (%) | Max Reports/Hour
Temperature | 10 | 3% | 12
Humidity | 6 | 2% | 12
Light | 4 | 1% | 12
Task
Decide reports per hour for each sensor (1–12) for 12 hours.
Calculate approximate battery usage
Calculate approximate importance coverage
Justify your strategy trade-offs.
Restrictions
Battery per sensor = 100%
Constraint: Total battery SUM ≥ 50% after 12h
Max reports per sensor = 12 per hour
Each sensor can report integer times per hour
Frequency of reports stays fixed once set

## Slide 39
References
PS, Akshatha, S. M. Dilip Kumar, and Venugopal KR. "MQTT implementations, open issues, and challenges: A detailed comparison and survey." International Journal of Sensors Wireless Communications and Control 12.8 (2022): 553-576.
Dizdarević, Jasenka, et al. "Benchmarking Performance of Various MQTT Broker Implementations in a Compute Continuum." 2024 IEEE 24th International Symposium on Cluster, Cloud and Internet Computing (CCGrid). IEEE, 2024.
Rao, K. Raghava, et al. "Energy efficiency analysis of LoRa and ZigBee protocols in wireless sensor networks." Revista Geintec 11.4 (2021): 2836-2849.
Hillar, Gaston C. Hands-On MQTT Programming with Python: Work with the lightweight IoT protocol in Python. Packt Publishing Ltd, 2018.
Alkwiefi, Maysam. "M2M Protocols: An Overview on LwM2M and XMPP Machine-to-Machine Protocols in IoT Context." 2024 IEEE/ACIS 24th International Conference on Computer and Information Science (ICIS). IEEE, 2024.
Shimizu, Kengo, Jun Yamaguchi, and Hidekazu Suzuki. "Data Management Scheme Using LwM2M in Optical Fiber Network Monitoring System." 2024 IEEE 13th Global Conference on Consumer Electronics (GCCE). IEEE, 2024.
Mafop, Nurul Najiha, Amar Zainal Abidin, and Hafizal Mohamad. "IoT-Based Monitoring System for Indoor Air Quality using Thingsboard." 2024 IEEE International Conference on Applied Electronics and Engineering (ICAEE). IEEE, 2024.
Jamil, Mohammad Newaj, et al. "Enabling industrial internet of things by leveraging distributed Edge-to-Cloud Computing: Challenges and opportunities." IEEE Access (2024).
Patil, Yatish. Azure IoT Development Cookbook: Develop and Manage Robust IoT Solutions. Packt Publishing Ltd, 2017.
Pranavasri, V. "Towards Scalable Architectures in oneM2M-based Interoperability deployments in Smart Cities." PhD thesis (2024).

## Slide 40
Questions/Discussion
?