## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 04

## Slide 2
The Hat Whispering Problem
Problem
  100 people in a line
  Each wearing a hat that is either red or blue
  Can’t see their own hat, only the hats in front
Rules
  People can say one color out loud in sequence from back to front.
  Everyone can hear the guesses of the people behind them.
  People can pre-agree on a strategy before the game starts.
Goal
  How to maximize the number of people who correctly guess their own hat color?

## Slide 3
The Hat Whispering Problem
The last person in line announces the parity of red hats in front (even/odd). Each subsequent person can deduce their own hat color by combining: The parity they hear, the visible hats in front, the previous guesses behind them
The power of local aggregation

## Slide 4
Επεξεργασία Δεδομένων στο Εσωτερικό του Δικτύου

## Slide 5
What is In-Network Data Processing?
IoT in-network data processing refers to the technique of performing data analysis, aggregation and filtering directly on or near the IoT devices within the network, rather than sending all raw data to a central cloud for processing.
Reduce network traffic
Lower latency
Increase efficiency

## Slide 6
The Compute Continuum
Cloud
Edge
Edge
Fog
Fog
Fog
IoT
IoT
IoT
IoT
Cloud computing: Traditional centralized computing where data processing and storage occur in remote data centers.
Edge Computing: Distributed computing framework that brings enterprise applications closer to data sources such as IoT devices or local edge servers.
Fog Computing: Decentralized computing infrastructure that brings computation and data storage closer to the network's extreme-edge, enabling real-time processing and reducing latency
Extreme-Edge, Far-Edge, On-Device or Mist Computing: Ultra-lightweight processing directly on constrained devices (sensors, small nodes), enabling immediate data processing at the source.

## Slide 7
5G Compute Continuum
The 5G Compute Continuum is an extension of the computing continuum concept that leverages 5G's low-latency, high-reliability network to create a seamless, distributed computing and storage environment that spans from the Mobile Edge Computing (MEC) nodes to the cloud.

## Slide 8
Case Study: Connected and Cooperative Vehicles
OBU (On-Board Unit, local processing in the vehicle)
  Tasks: immediate collision detection, lane keeping, emergency braking, obstacle avoidance.
  Pros: ultra-low latency, fast reaction.
  Cons: limited computing power, energy constraints.
RSU (Road Side Unit, edge/fog processing)
  Tasks: traffic flow optimization, accident detection, local route planning, aggregating data from multiple vehicles.
  Pros: coordinate multiple vehicles, reduces cloud load.
  Cons: coverage limited to RSU range, potential handover delays.
Central Cloud
  Tasks: long-term traffic analysis, map updates, predictive analytics, fleet management.
  Pros: unlimited computation and storage, global optimization.
  Cons: high latency, bandwidth intensive
Trade-Offs
Latency vs computation power
Bandwidth vs data volume
Reliability vs coverage

## Slide 9
Core Techniques for In-Network Processing
Technique | Purpose | Example Tools / Methods | Benefit
Filtering | Remove noise or irrelevant readings | Thresholding, moving average | Reduces data volume
Aggregation | Combine multiple sensor readings | Mean, median, count, min/max | Simplifies information
Compression | Encode data efficiently | Run-length, delta, Huffman | Saves bandwidth
Event Detection / Stream Analytics | Identify anomalies or specific events as data arrives | CEP (Complex Event Processing), rule-based triggers | Enables fast response
Data Fusion | Combine data from multiple sensors for richer insight | Kalman filters, probabilistic models | Improves accuracy and robustness

## Slide 10
Hands-on Example: In-Network Processing
Scenario
  Environmental sensors may temporarily fail or report no values.
  Local decisions (e.g., alarms) must continue functioning.
  We estimate missing readings before sending data upstream.
Strategy | How it Works | Pros | Cons / Notes
Remove / Ignore | Drop readings with NaN | Simple | Reduces data points, may lose info
Linear Interpolation | (prev + next) / 2 | Smooths trends | Requires both previous and next values
Neighbor Average | Average of other sensors at same timestamp | Uses spatial redundancy | Assumes nearby sensors are correlated
Carry Forward / Last Observation | Use last known reading | Very simple, fast | May be stale if trends change quickly
Carry Backward / Next Observation | Use next known reading | Useful if only past unavailable | Impractical in real-time systems
Weighted Neighbor / Time + Space | Weighted average of nearby sensors & past | More nuanced | Slightly more complex, still local
Minimum / Maximum Fill | Use min/max of neighbors or historical range | Conservative / safe for thresholds | Can over/underestimate actual value
Median Fill | Use median of neighbors / previous readings | Robust to outliers | Ignores temporal trend

## Slide 11
Hands-on Example: In-Network Processing
Time | Sensor A (°C) | Sensor B (°C) | Sensor C (°C)
10:00 | 23.5 | 22.7 | 22.4
10:05 | 24.6 | NaN | 22.5
10:10 | NaN | 21.8 | 23.6
10:15 | 22.7 | 22.9 | NaN
10:20 | 23.8 | NaN | 22.7
Task
  Choose a strategy for the NaNs.
  Fill all missing values in table.
  Compute local average at each timestamp
  Decide if local action is triggered (e.g., average > 23°C → alert).

## Slide 12
Basics on Kalman Filtering
Core Idea:
  Smooths noisy sensor readings locally at the edge
  Combines:
    Prediction: what the system expects based on past measurements
    Measurement: what the sensor actually reports
Produces a more accurate estimate of the true value
Helps reduce false alerts and bandwidth usage by sending only cleaned data to the cloud
Example:
  3 temperature sensors send readings every 2 seconds
  Some readings are noisy or faulty
  Kalman filter at the edge:
    Smooths readings → stable average
    Detects anomalies → triggers alerts only when necessary
    Sends only filtered average to the cloud
https://kalmanfilter.net/

## Slide 13
Key Frameworks & Platforms
Framework / Platform | Focus / Strengths | Reference
EdgeX Foundry | Open-source, device interoperability, modular microservices | https://www.edgexfoundry.org/
AWS IoT Greengrass | Cloud integration, Lambda functions at edge | https://aws.amazon.com/greengrass/
Azure IoT Edge | Cloud-native, deploy AI/ML modules locally | https://github.com/Azure/iotedge
ThingsBoard Edge | Open-source, dashboard & analytics at edge | https://thingsboard.io/products/thingsboard-edge/
Apache Edgent | Lightweight edge analytics, stream processing on constrained nodes | https://incubator.apache.org/projects/edgent.html

## Slide 14
Quick Demo: Node-RED
# Pull the official image
docker pull nodered/node-red
# Run the container, map ports and mount local volume for persistence
docker run -it -p 1880:1880 -v node_red_data:/data --name nodered-demo nodered/node-red
Node-RED is a low-code, flow-based development tool for wiring together devices, APIs, and online services in IoT systems.
Core Idea: Instead of writing long code, users drag and connect nodes to build data flows that handle data collection, processing, and action.
Key Features:
  Visual programming interface – build flows using a web-based editor
  Runs anywhere – from cloud to edge devices (e.g., Raspberry Pi, gateways)
  Supports protocols – MQTT, HTTP, WebSockets, Modbus, etc.
  Built-in processing – filter, aggregate, and transform IoT data locally
  Extensible – thousands of community nodes and integrations (e.g., AWS, Azure, dashboards)
Demo Setup:
  Node-RED running in Docker on my laptop
  Access dashboard via browser: http://<my-IP>:1880/ui

## Slide 15
Quick Demo: Node-RED
Network Setup
  Sensors generate temperature readings (some may be faulty / NaN)
  Edge server cleans data, aggregates, computes average, predicts next value
  Alerts:
    Sensor Error → flags faulty readings
    Overheat → triggers if current or predicted average exceeds threshold
  Data flow: Sensors → Edge → Dashboard → Cloud (optional)
Dashboard Elements (Vertical Layout)
  Sensor Values (Text) → latest reading for each sensor
  Current Average (Gauge) → real-time average of all sensors
  Predicted Average (Gauge) → next average predicted by edge
  Sensor Error Alert (Text) → highlights NaN or faulty readings
  Overheat Alert (Text) → warns if current/predicted average exceeds threshold
Observations & Discussion
  Filtering reduces noise → stable readings
  Aggregation smooths signal → reliable average
  Prediction shows future trend → proactive alerting
  Low latency → dashboard updates instantly
Food for thought
  Which readings could be filtered further?
  How much bandwidth would be saved if only filtered data reached the cloud?

## Slide 16
Advanced Processing & Research Trends
Edge AI / TinyML
  Perform machine learning inference directly on constrained devices (microcontrollers, edge nodes)
  Enables real-time decision-making without sending all data to the cloud
Federated Learning
  Train shared models collaboratively while keeping raw data local
  Central server aggregates local model updates → updated global model
Energy-efficient Algorithms
  Minimize computation and communication overhead
  Extend device battery life and reduce network load
Distributed Stream Processing
  Detect and react to events in real-time across multiple edge nodes
  Supports scalable, low-latency IoT analytics

## Slide 17
Lightweight Machine Learning at the Edge
Rainey, James, et al. "Food recognition and segmentation using embedded hardware." Applications of Digital Image Processing XLVII. Vol. 13137. SPIE, 2024.
Running lightweight machine learning models directly on edge devices
Enables local inference without cloud dependency.
Works even in offline or low-connectivity environments
Technologies & Frameworks:
  TensorFlow Lite / TensorFlow Lite Micro – Optimized for microcontrollers and embedded systems
  PyTorch Mobile / Edge – Deploy compact neural nets to mobile or embedded hardware
  Edge Impulse – Complete TinyML platform for collecting data, training, and deploying models
  AWS IoT Greengrass ML Inference – Run ML models locally on edge devices managed by AWS
  Intel OpenVINO – Accelerates inference on Intel CPUs, VPUs, and embedded systems
  Google Coral / Edge TPU – Specialized hardware for ultra-efficient local inference
  NVIDIA Jetson (Nano / Xavier) – Edge AI platform for high-performance local analytics
  Arduino / ESP32 with TinyML – Microcontroller boards running simple neural networks on-device
Use Cases:
  Gesture recognition – Smart wearables, human–machine interaction
  Sound recognition – Detect anomalies in equipment, voice triggers
  Predictive maintenance – Identify early failure signs locally
  Environmental monitoring – Local detection of pollution or gas leaks
  Smart health – On-device heart rate or motion anomaly detection.

## Slide 18
Federated Machine Learning
Core Idea:
  Train shared machine learning models without sending raw sensor data to the cloud
  Each edge node trains locally on its own data
  Only model updates (gradients or weights) are sent to a central server
  Central server aggregates updates → updated global model → sent back to nodes
Benefits in IoT:
  Privacy-preserving: raw data never leaves local devices
  Bandwidth-efficient: only model updates are transmitted
  Scalable: multiple edge nodes can collaborate without centralizing all data
  Real-time adaptation: nodes can update models based on local changes
Nguyen, Dinh C., et al. "Federated learning for internet of things: A comprehensive survey." IEEE communications surveys & tutorials 23.3 (2021): 1622-1658.

## Slide 19
Smart City IoT Competition: A Simulation Game
Game Overview
Teams: Team A vs. Team B
Sensors: 8 different types
Processing options:
  On-Device
  Local Edge
  Wide Area Edge,
  Country-Wide Cloud
Rounds: 100, each round lasts 30 seconds
First round starts after 60 seconds
Events occur randomly each round affecting sensors
Cumulative score shows overall performance

## Slide 20
Smart City IoT Competition: A Simulation Game
Events affect one or multiple sensors
Event types: traffic spikes, pollution alerts, intrusions, heavy rain, noise surge, energy spikes
Events apply multipliers to latency, energy, and network cost
Some events grant critical bonus points for fast processing
Not all events are predictable; teams must strategize

## Slide 21
Smart City IoT Competition: A Simulation Game
Sensor Placement Choice
  Each sensor can be processed locally, at edge, or in cloud.
  Placement affects latency, energy consumption, and network cost.
  These factors determine a baseline score for the sensor in a round.
Events / Incidents
  Random events affect certain sensors (e.g., traffic spike, intrusion, rain).
  Events modify sensor scores via multipliers on latency, energy, and network.
  Some events grant critical bonuses for timely, local processing.
Round Score Aggregation
  For each round, sensor scores are summed to give the team’s round score.
  If no event occurs, a default fraction (e.g., 80%) of the maximum base score is used.
Cumulative Score
  Round scores are added over all rounds to yield cumulative score.
  Cumulative score is the main performance metric and what the live graph shows.

## Slide 22
Smart City IoT Competition: A Simulation Game
Sensor | On-Device | Local Edge | Wide Area Edge | Country-Wide Cloud
Traffic Camera | Latency: 2 ms Energy: 10 Network: 0 | Latency: 10 ms Energy: 5 Network: 2 | Latency: 25 ms Energy: 3 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Air Quality Sensor | Latency: 2 ms Energy: 8 Network: 0 | Latency: 10 ms Energy: 4 Network: 2 | Latency: 25 ms Energy: 2 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Security Camera | Latency: 2 ms Energy: 12 Network: 0 | Latency: 12 ms Energy: 6 Network: 3 | Latency: 30 ms Energy: 3 Network: 6 | Latency: 55 ms Energy: 1 Network: 12
Water Level Sensor | Latency: 2 ms Energy: 7 Network: 0 | Latency: 10 ms Energy: 3 Network: 2 | Latency: 25 ms Energy: 2 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Noise Sensor | Latency: 2 ms Energy: 5 Network: 0 | Latency: 10 ms Energy: 2 Network: 2 | Latency: 25 ms Energy: 1 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Parking Sensor | Latency: 2 ms Energy: 6 Network: 0 | Latency: 10 ms Energy: 3 Network: 2 | Latency: 25 ms Energy: 2 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Weather Sensor | Latency: 2 ms Energy: 4 Network: 0 | Latency: 10 ms Energy: 2 Network: 2 | Latency: 25 ms Energy: 1 Network: 5 | Latency: 50 ms Energy: 1 Network: 10
Energy Meter Sensor | Latency: 2 ms Energy: 5 Network: 0 | Latency: 10 ms Energy: 3 Network: 2 | Latency: 25 ms Energy: 2 Network: 5 | Latency: 50 ms Energy: 1 Network: 10

## Slide 23
Smart City IoT Competition: A Simulation Game
Event Name | Sensors Affected | Effects / Multipliers | Critical Bonus | Description
Traffic Spike | Traffic Camera | Latency × 2 | 5 | Rush hour congestion occurs
Pollution Alert | Air Quality Sensor, Noise Sensor | Network × 2 | 4 | Construction dust affects air & noise readings
Intrusion Attempt | Security Camera | Latency × 1.5 | 10 | Security camera must respond immediately
Heavy Rain | Traffic Camera, Water Level Sensor | Latency × 1.5 | 4 | Storm affects traffic & water sensors
Noise Surge | Noise Sensor, Parking Sensor | Energy × 2 | 2 | Large noise near sensors & parking disruption
Energy Grid Spike | Energy Meter Sensor, Weather Sensor | Latency × 1.2, Network × 1 | 5 | Sudden energy demand and weather changes
Combined Emergency | Traffic Camera, Security Camera, Energy Meter Sensor | Latency × 2, Network × 1 | 8 | Multiple incidents at once
Minor Sensor Glitch | All sensors | Energy × 1.5 | 1 | Small random sensor errors

## Slide 24
Smart City IoT Competition: A Simulation Game
Consider latency vs. energy vs. network cost
Some sensors are more critical during certain events
Hybrid strategies often outperform uniform choices
No perfect solution; aim for balanced placement
Discuss and defend your team’s strategy after rounds

## Slide 25
References
Ali, N., Aloi, G., De Rango, F., Savaglio, C., & Gravina, R. (2025). Edge-cloud continuum driven industry 4.0. Procedia Computer Science, 253, 2586-2594.
Amadeo, Marica, and Giuseppe Ruggeri. "Exploring in-network computing with information-centric networking: review and research opportunities." Future Internet 17.1 (2025): 42.
Ficco, Massimo, et al. "Federated learning for IoT devices: Enhancing TinyML with on-board training." Information Fusion 104 (2024): 102189.
Tekin, N., Aris, A., Acar, A., Uluagac, S., & Gungor, V. C. (2024). A review of on-device machine learning for IoT: An energy perspective. Ad Hoc Networks, 153, 103348.
Chai, X., Lee, B. G., Hu, C., Pike, M., Chieng, D., Wu, R., & Chung, W. Y. (2025). IoT-FAR: A multi-sensor fusion approach for IoT-based firefighting activity recognition. Information Fusion, 113, 102650.
Lekić, Milica, and Gordana Gardašević. "IoT sensor integration to Node-RED platform." 2018 17th International Symposium Infoteh-Jahorina (Infoteh). IEEE, 2018.
Kianpisheh, S., & Taleb, T. (2022). A survey on in-network computing: Programmable data plane and technology specific applications. IEEE Communications Surveys & Tutorials, 25(1), 701-761.

## Slide 26
Questions/Discussion
?