## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 07

## Slide 3
https://www.youtube.com/watch?v=pDoar4zh5tI

## Slide 4
Επεξεργασία στις Παρυφές του Δικτύου και Προκλήσεις

## Slide 5
Edge Computing – Unveiling the mystery
Quiz: Define Edge Computing

## Slide 6
Defining Edge Computing
Edge Computing: Processing data near the source of data, such as edge devices or gateways, rather than in the cloud.
Fog Computing: A hierarchical layer between edge and cloud that distributes computation, storage, and networking across multiple intermediate nodes.
Cloud Computing: Centralized processing of data in remote data centers, accessible over the internet.
MEC (Multi-access Edge Computing): 5G-enabled edge computing integrated with the network, allowing computation and storage at the edge of the mobile network.
Extreme Edge Computing (On-device Computing): Processing data directly on the device itself, such as sensors or microcontrollers, without sending it elsewhere.

## Slide 7
IoT Edge vs 5G Edge (1)
Feature/Metric | IoT Edge | 5G Edge (MEC)
Latency | Low, typically tens of ms | Ultra-low, sub-ms to few ms possible
Bandwidth | Limited, dependent on local connectivity (Wi-Fi, LPWAN) | High, 5G network enables multi-Gbps
Deployment | Local devices, gateways, microcontrollers | Integrated into mobile network infrastructure (base stations, edge data centers)
Compute Resources | Limited CPU/GPU, memory constrained | High compute capacity, near cloud-level
Network Integration | Independent, may use Wi-Fi, LoRaWAN, Ethernet | Deeply integrated with 5G RAN and core network
Mobility Support | Low to moderate (fixed devices or local roaming) | High, seamless handover for mobile users/devices

## Slide 8
IoT Edge vs 5G Edge (2)
Feature/Metric | IoT Edge | 5G Edge (MEC)
Reliability & QoS | Moderate, device/gateway-dependent | Very high, SLA-driven, network-assisted reliability
Security | Localized, device-level security | Network-assisted security, slicing, MEC-based isolation
Use Cases | Smart homes, environmental monitoring, sensors | AR/VR, autonomous vehicles, industrial IoT, smart cities
Data Processing | Mainly aggregation, filtering, local analytics | Real-time analytics, AI inference, offloading to cloud if needed
Scalability | Limited, constrained by device/gateway | High, can handle massive connected devices via 5G infrastructure
Energy Consumption | Low-power design (battery or constrained devices) | Higher energy due to dense compute and network integration

## Slide 9
Why Edge?
Data Privacy
Energy Efficiency
Scalability
Reliability (Single-Point-of-Failure)
Bandwidth efficiency
Autonomous (offline) operation w/o cloud
Delay Reduction
Security
Can you get examples for each benefit?

## Slide 10
Use-case: SmartSantander - City‑Scale Edge IoT Testbed
https://smartsantander.eu/
1. Use-Case Overview
  Large-scale smart city testbed in Santander with thousands of sensors monitoring environmental conditions, traffic and parking.
2. Edge Deployment
  Three-tier architecture: sensors → local gateways → edge servers → central servers.
  Gateways aggregate, preprocess and temporarily store data before forwarding.
3. IoT Edge Functionality
  Edge gateways perform local filtering, aggregation and event detection.
  Reduces data volume sent to central servers and enables near-real-time monitoring.
4. Edge Benefits
  Low latency alerts (e.g., traffic incidents, parking availability).
  Reduced network congestion and cloud load.
  Enables offline or intermittent operation if connectivity is limited.

## Slide 11
Use-case: Siemens+AWS Smart Factories Powered by Edge
https://blog.siemens.com/2025/03/smart-manufacturing-at-scale-siemens-and-aws-build-a-data-foundation-for-the-future/
1. Use-Case Overview
  Industrial manufacturing with hybrid edge-to-cloud infrastructure for real-time machine monitoring and analytics.
2. Edge Deployment
  Industrial Edge devices collect machine data on-site.
  AWS IoT SiteWise Edge integrates with local devices for processing and cloud synchronization.
3. IoT Edge Functionality
  Local edge nodes handle real-time analytics, anomaly detection and predictive maintenance.
  Edge decides what data to send to the cloud, optimizing bandwidth.
4. Edge Benefits
  Ultra-low latency for critical factory processes.
  Reduces bandwidth and cloud storage by processing raw data locally.
  Enhances operational reliability during network outages.
  Enables scalable deployment across multiple factory sites.

## Slide 12
Use-case: Deep North + NVIDIA Smart Retail Insights at the Edge
https://www.nvidia.com/content/dam/en-zz/Solutions/industries/retail/retail-solution-showcase-deep-north-web.pdf
1. Use-Case Overview
  Retail stores use AI-driven video analytics to understand customer behavior, occupancy and engagement.
2. Edge Deployment
  NVIDIA EGX/Jetson devices deployed in-store.
  IP cameras feed video streams to local edge nodes for processing.
3. IoT Edge Functionality
  Edge performs AI inference on video streams locally (occupancy counts, heatmaps, dwell times).
  Only processed insights and summary metrics are sent to central dashboards.
4. Edge Benefits
  Real-time decision making (staff allocation, crowd management).
  Preserves customer privacy by keeping video data on-site.
  Reduces bandwidth and cloud processing requirements.
  Scalable across multiple store locations with consistent insights.

## Slide 13
Edge Frameworks for IoT (1)
https://learn.microsoft.com/en-us/azure/iot-edge/tutorial-monitor-with-workbooks
Description:
  Software platforms for deploying, orchestrating and managing IoT workloads at the edge
  Run applications locally, close to sensors and devices
  Examples: AWS Greengrass, Azure IoT Edge, EdgeX Foundry, KubeEdge
Motivation:
  Reduce latency by processing data near the source
  Save bandwidth by sending only necessary data to the cloud
  Enhance reliability when cloud connectivity is intermittent
  Enable local AI/ML inference and analytics
  Standardize heterogeneous devices and protocols
Core Functionality:
  Deploy, monitor and update edge applications
  Local data processing, filtering, and aggregation
  Device-to-cloud communication and messaging
  Security: authentication, encryption, access control
  Seamless integration with cloud services
Key Takeaway:
  Bridge devices and cloud for scalable, secure
  and efficient edge intelligence
  Provide the software backbone for
  task placement across device, edge, fog, and cloud layers

## Slide 14
Edge Frameworks for IoT (2)
Framework | Core Functionality | Deployment Model | Processing & Analytics | Languages Supported | ML/AI Support | Containerization/Runtime
AWS Greengrass | Local device data processing, IoT messaging, lambda functions | Cloud-managed, edge devices (Greengrass Core) | Stream processing, Lambda-based local analytics | Python, Node.js, Java, C | Supports SageMaker models at edge | Docker optional, native runtime for Lambdas
Azure IoT Edge | Edge modules deployment, device-to-cloud integration | Cloud-managed, edge devices with IoT Edge runtime | Stream analytics, ML inference, custom modules | C#, Python, Java, Node.js | Supports ONNX and Azure ML models | Docker containers for modules
EdgeX Foundry | Open-source microservices-based edge framework | Edge gateway / device deployment | Sensor data ingestion, filtering, analytics | Go, Java, C, Python | Supports ML via microservices | Docker containers (compose-based), microservices architecture

## Slide 15
Edge Frameworks for IoT (3)
Framework | Core Functionality | Deployment Model | Processing & Analytics | Languages Supported | ML/AI Support | Containerization/Runtime
KubeEdge | Kubernetes-native edge orchestration | Edge nodes + cloud Kubernetes | IoT device management, edge ML inference, real-time analytics | Go | Supports containerized ML workloads | Docker/containerd, Kubernetes-native
thin-edge.io | Lightweight edge agent for constrained devices | Edge devices with lightweight agent | Telemetry collection, MQTT forwarding, lightweight analytics | Rust, C | Supports ML inference via integration with cloud | Lightweight container support, native agent-based
Eclipse Kura | IoT gateway framework for edge | Gateway devices (Linux/ARM) | Device data aggregation, local rule-based analytics | Java | Supports integration with ML models via Java libraries | OSGi-based modular containers

## Slide 16
Edge Deployments: IoT Edge Gateways (Low-Power Field Devices)
Typical hardware:
  ARM-based industrial gateways
    Advantech, AAEON, Siemens IOT2040
  CPU: Dual/Quad-core ARM Cortex-A7/A53
  RAM: 512 MB–2 GB
  Storage: embedded Multi-Media Card 4–32 GB
Processing capacity:
  Low
  Suitable for
    protocol translation
    basic filtering
    lightweight analytics
Scalability:
  Limited to dozens of sensors
  Often used as Tier-1 edge nodes feeding upstream servers
Energy consumption:
  Very low (5–15 W)
  Can be powered by solar or battery
    Siemens IOT2040
  ARM Cortex-A7/A53

## Slide 17
Edge Deployments: Embedded AI Edge Units
Typical hardware:
  NVIDIA Jetson Nano, Xavier NX, Orin
  GPU: CUDA cores (128 → 2048)
  CPU: Quad/Octa-core ARM Cortex-A57/A78AE
  RAM: 4–32 GB
  AI performance: 0.5-275 TOPS (depending on model)
Processing capacity:
  Medium–High for local inference
  Real-time video analytics, robotics, IoT AI workloads
Scalability:
  Supports multi-camera setups, autonomous robots, local ML pipelines
  Can cluster a few units for higher throughput
Energy consumption:
  10–60 W depending on model & load

## Slide 18
Edge Deployments: Ruggedized Edge Servers
Typical hardware:
  Dell EMC Edge Gateway 3200/HPE Edgeline EL300
  CPU: Intel Xeon D/Core i7/i9
  RAM: 16–128 GB
  Storage: NVMe SSD 512 GB–4 TB
  Optional accelerators: Intel Movidius VPUs, small GPUs
Processing capacity:
  High; handles multiple containerized services, local data pipelines
  Suitable for industrial IoT, retail analytics, smart buildings
Scalability:
  Supports dozens to hundreds of devices
  Kubernetes-ready (K3s/KubeEdge)
Energy consumption:
  Medium (60–250 W) depending on configuration
Dell EMC Edge Gateway 3200/HPE
Intel Xeon i7-6700

## Slide 19
Edge Deployments: Mini Edge Data Centers
Micro DC
NVIDIA A100
Typical hardware:
  1–3 cabinet micro-DC units (e.g., Schneider Micro DC, Vapor Edge Module)
  Compute: Several rack servers (Xeon/EPYC CPUs)
  Optional: NVIDIA A100/A30 GPUs, FPGAs, SmartNICs
  Fabric: 10–100 GbE switches or optical interconnect
Processing capacity:
  Very high; supports distributed edge cloud services
  Ideal for enterprise campuses, telco edge, smart factories
Scalability:
  Scales to dozens of servers per rack
  Can run full Kubernetes/VM environments
Energy consumption:
  High (1–10 kW per rack)
  Requires cooling (air/liquid), UPS, monitoring

## Slide 20
Edge Deployments: Telco MEC
Typical hardware:
  Standardized racks co-located with base stations
  CPU: Multi-socket Xeon/EPYC
  GPU/FPGA accelerators for RAN & inference
  Storage: Tiered NVMe/SSD arrays
  Network: Ultra-low-latency fronthaul (C-RAN, O-RAN)
Processing capacity:
  Extremely high for low-latency workloads
  Designed for AR/VR, V2X, robotics, real-time control loops
Scalability:
  Supports thousands of mobile/IoT endpoints
  Integrated with operator cloud backbone
Energy consumption:
  High (5–20 kW per MEC site)
  Dependent on available telecom infrastructure

## Slide 21
Edge Deployments: Comparison
Edge Tier | Example Hardware | Processing Capacity | Scalability | Energy Use | Indicative Use-Cases
IoT Gateway | Siemens IOT2040 | Low | Low | Very Low | Smart building sensors (temperature, lighting, occupancy control), Industrial IoT (vibration/temperature monitoring for predictive maintenance), Retail shelf monitoring (simple inventory and alert systems)
Embedded AI | NVIDIA Jetson Orin | Medium–High | Medium | Low–Medium | Autonomous robots in factories (real-time navigation and collision avoidance), Video analytics (at retail stores for customer counting or behavior analysis), Smart cameras (traffic monitoring and object detection)
Rugged Edge Server | HPE Edgeline | High | Medium–High | Medium | Local aggregation of multiple industrial IoT devices with real-time analytics, Edge-based energy management in microgrids, Manufacturing quality control with AI/ML inference pipelines
Mini Edge DC | Schneider Micro DC | Very High | High | High | Campus or factory-scale edge cloud for multi-application orchestration, Smart city control (traffic, lighting, environmental monitoring), Healthcare edge hub for aggregating patient monitoring devices and running analytics
Telco MEC | 5G MEC Rack | Ultra-High | Very High | Very High | AR/VR gaming or enterprise applications requiring ultra-low latency, Connected vehicles/V2X (real-time traffic, navigation and safety analytics), High-frequency trading or financial applications needing sub-ms response times

## Slide 22
Group Discussion
“If edge computing is so amazing, why aren’t Netflix, Tesla and your smart toaster all running everything locally?”

## Slide 23
Group Discussion
Edge capacity is limited … CPUs, GPUs, memory and storage cannot match cloud-scale.
Ops cost skyrockets … managing updates, failures and security across many edge sites is expensive.
Some workloads need global data … training, aggregation, and cross-site analytics live better in the cloud.
Distributed nodes add complexity … synchronization, consistency and coordination get harder at scale.
Energy, heat, and space are constrained … edge boxes cannot host large compute clusters.
Security posture varies … physical exposure and heterogeneous environments increase risk.
No single layer is perfect.
So how we decide where to place our tasks?

## Slide 24
Task Placement/Offloading in IoT – The Optimization Problem
The placement problem
  Deciding where to process data
  On-device, at the edge, or in the cloud
  A core design decision in IoT systems.
  Impacts latency, bandwidth, energy consumption, security and cost.
Key Points:
  On-device: Processing happens directly on sensors or actuators (extreme edge).
  Edge: Processing occurs on local gateways or micro data centers.
  Cloud: Data is sent to centralized servers for storage and computation.
Trade-offs exist
  faster responses vs richer analytics
  energy efficiency vs compute power
  local privacy vs cloud aggregation.

## Slide 25
Trade-off: Latency vs Compute
Trade-Off Description
  Placing processing locally (on-device/edge) reduces latency but may be limited by compute resources.
  Sending data to cloud increases available compute but adds latency.
Focus on Latency
  Critical for real-time or safety-critical tasks such as autonomous vehicles, robotics, industrial controls.
  Place processing close to the source to ensure fast responses.
Focus on Compute
  Needed when tasks require heavy analytics, AI inference, or complex processing beyond local device capacity.
  Edge or cloud is preferred when compute demand exceeds local resources.
Typical Cases
  On-device: immediate sensor reactions, emergency stops.
  Edge: ML inference on aggregated sensor data, real-time control loops.
  Cloud: long-term analytics, large model training, cross-site optimization.

## Slide 26
Trade-off: Bandwidth vs Energy
Trade-Off Description
  Transmitting all data to cloud consumes network bandwidth and may congest connections.
  Local processing saves bandwidth but consumes device or gateway energy.
Focus on Bandwidth
  When data volume is high (e.g., video streams, LIDAR, high-frequency sensors).
  Edge aggregation or filtering reduces data sent over network, avoiding congestion.
Focus on Energy
  Battery-powered or constrained devices cannot run heavy processing continuously.
  Lightweight on-device analytics or selective transmission preserves energy.
Typical Cases
  On-device: threshold detection, event-triggered sampling, basic preprocessing.
  Edge: intermediate aggregation, AI inference, anomaly detection before sending to cloud.
  Cloud: historical trend analysis, batch processing, full dataset analytics.

## Slide 27
Trade-off: Security & Privacy vs Flexibility
Trade-Off Description
  Processing locally or on edge protects sensitive data but can limit flexibility in updates or scaling.
  Cloud offers centralized management and scalable analytics, but increases exposure risk.
Focus on Security/Privacy
  Personal health data, video surveillance, industrial secrets should be processed close to source.
  Reduces chance of leaks or unauthorized access.
Focus on Flexibility
  Frequent updates, multi-site coordination and cloud-based analytics benefit from centralized processing.
Typical Cases
  On-device: medical wearables, smart locks, cameras with local analytics.
  Edge: industrial control systems, smart city gateways, retail analytics.
  Cloud: cross-site dashboards, long-term trend analysis, centralized AI training.

## Slide 28
Placement Problem Modelling – Using Integer Linear Programming (ILP)
Integer Linear Programming (ILP)?
  A mathematical optimization framework where objective function and constraints are linear.
  Some or all variables are constrained to be integers (often 0/1 → decisions).
  Commonly used to model selection, assignment and resource allocation problems.
Why ILP Fits IoT/Edge/Cloud Placement
  Placement is fundamentally a discrete decision problem:
    Where should each task run? → device / edge / fog / cloud
  Constraints naturally map to linear forms:
    compute limits
    memory limits
    bandwidth budgets
    privacy/security requirements
    availability or cost limits
  Objective can represent:
    minimizing latency
    maximizing privacy
    minimizing energy
    maximizing QoS
    or multi-criteria tradeoffs (via weighted sum).

## Slide 29
Placement Problem Modelling - Define IoT Tasks
Concept:
  Identify all tasks T={T1,T2,...,Tn} generated by IoT devices that need processing.
  Tasks could include sensor monitoring, AI inference, video analytics, actuation, etc.
Example:
  3 tasks in a smart factory:
    T1=Temperature monitoring
    T2=Vibration-based predictive maintenance
    T3=Video stream analysis
Goal: Decide where each task should run: device, edge, or cloud.

## Slide 30
Placement Problem Modelling - Define Decision Variables
Task | Device | Edge | Cloud
T1=Temperature | 1 | 0 | 0
T2=Vibration | 0 | 1 | 0
T3=Video | 0 | 1 | 0
Example Solution

## Slide 31
Placement Problem Modelling - Define Constraints
Concept: Constraints define feasible assignments in terms of resources, latency, or other requirements.
Example:
  Edge node has 10 compute units.
  Task assignments:
    Temperature = 2 units, Vibration = 5 units, Video = 4 units → total = 11
    Exceeds capacity!

## Slide 32
Placement Problem Modelling - Define Objective Function
Example: Minimize total latency
The Objective Function defines the parameter we want to optimize (minimize or maximize)
Task | Device | Edge | Cloud
T1=Temperature | 1 ms | 5 ms | 20 ms
T2=Vibration | 3 ms | 5 ms | 25 ms
T3=Video | 10 ms | 15 ms | 50 ms
Example: Minimize total latency and total energy and total bandwidth (multi-objective) with different weights (a, b, c)

## Slide 33
Placement Problem Modelling - Solutions
Concept
  Small problems can be solved manually or with simple heuristics.
Large problems use optimization techniques:
  Linear programming / Integer Linear Programming (ILP)
  Greedy heuristics
  Metaheuristics (genetic algorithms, simulated annealing)
Solving Steps (Example):
  Input tasks, resource requirements, latency/energy/bandwidth estimates.
  Define binary placement variables and constraints.
  Feed ILP to solver (e.g., CPLEX, Gurobi, OR-Tools).
  Solver outputs Xi,j​ for each task.
Task | Device | Edge | Cloud
Temperature | 1 | 0 | 0
Vibration | 0 | 1 | 0
Video | 0 | 1 | 0
Example outcome that minimizes latency while respecting compute constraints.

## Slide 34
Exercise: Model the Placement Problem into ILP
Scenario:
  5 IoT tasks in a smart factory.
  4 layers: Device, Edge, Fog, Cloud.
  Goal: maximize overall privacy while respecting compute, memory and bandwidth constraints.
Task | Compute (units) | Memory (MB) | Bandwidth (MB/s) | Privacy Score Device | Privacy Score Edge | Privacy Score Fog | Privacy Score Cloud
T1: Temp Monitoring | 2 | 50 | 1 | 10 | 7 | 5 | 1
T2: Vibration Analysis | 4 | 100 | 5 | 9 | 6 | 4 | 1
T3: Video Analytics | 6 | 200 | 20 | 10 | 7 | 5 | 1
T4: Machine Status | 3 | 80 | 2 | 8 | 6 | 4 | 1
T5: Pred. Mainten. | 5 | 150 | 10 | 9 | 6 | 5 | 1
Layer | Compute Units | Memory (MB) | Bandwidth Limit (MB/s)
Device | 10 | 300 | N/A
Edge | 15 | 500 | 30
Fog | 20 | 600 | 50
Cloud | 50 | 2000 | 100
ToDO:
  Decision Variables and their Restrictions
  System Constraints
  Objective Function

## Slide 35
Exercise: Model the Placement Problem into ILP (1)

## Slide 36
Exercise: Model the Placement Problem into ILP (2)

## Slide 37
Exercise: Model the Placement Problem into ILP (3)
Objective Function:

## Slide 38
Exercise: Model the Placement Problem into ILP (4)
Solve using Python pulp
https://pypi.org/project/PuLP/
Result - Optimal solution found
Objective value: 40.00000000
Enumerated nodes: 0
Total iterations: 1
Time (CPU seconds): 0.02
Time (Wallclock seconds): 0.02
Total time (CPU seconds): 0.05 (Wallclock seconds): 0.05
Status: Optimal, Task Assignments:
  T1 -> Device
  T2 -> Device
  T3 -> Edge
  T4 -> Device
  T5 -> Edge
Total Privacy Score: 40.0

## Slide 39
Limits of ILP for IoT Edge/Cloud Task Placement
NP-hard scaling
  ILP solve time grows exponentially with number of tasks, nodes, constraints
  Impractical for large IoT fleets (e.g., 10k+ devices).
Static snapshot assumption
  ILP typically models a single time-step
  Does not handle dynamic workloads, fluctuating connectivity, or mobility.
Perfect information requirement
  Assumes all params (compute, network, etc) are accurate
  Real systems exhibit uncertainty and noise.
Hard to model non-linear real-world behaviors
  Latency, energy consumption, RF interference, thermal throttling, congestion
  Inherently non-linear
  ILP forces linearization.
Centralized optimization overhead
  Solving centrally introduces communication overhead
  Becomes a bottleneck and single point of failure.
Limited real-time applicability
  Re-solving the ILP every few secs in changing environments is often infeasible.

## Slide 40
Task Placement Research Directions (SotA & Beyond)
1. Heuristics & Metaheuristics
  Genetic algorithms, simulated annealing, ant-colony optimization
  Scalable approximations for large IoT deployments.
  Fast greedy placement + local search
  Real-time operation with acceptable sub-optimality.
2. Distributed & Federated Optimization
  Multi-agent placement algorithms running across device–edge–cloud
  Reduces central bottlenecks; supports dynamic and large-scale systems.
  Consensus-based optimization (federated reinforcement).
3. Reinforcement Learning for Placement
  DRL policies learn where to place tasks based on observations
  Handles non-linear, stochastic environments better than ILP.
  Online learning adapts to mobility, congestion, energy depletion.
4. Multi-objective and Context-Aware Optimization
  Pareto optimization of latency–energy–privacy–cost
  Utility-based frameworks
  Stochastic optimization under uncertainty (e.g., connectivity loss)
5. Hierarchical & Intent-Based Orchestration (Rule Engines)
  Layered controllers: device-level → edge cluster → cloud coordinator
  Operators specify high-level service intents (e.g., “maximize privacy”)
  The system translates them into placement policies automatically.
6. AI-Augmented Solvers
  Neural ILP warm-starting
  Graph neural networks predicting good feasible solutions

## Slide 41
On Edge Computing for IoT
  Alanhdi, Amad, and László Toka. "A survey on integrating edge computing with ai and blockchain in maritime domain, aerial systems, iot, and industry 4.0." Ieee Access 12 (2024): 28684-28709.
  Sodiya, Enoch Oluwademilade, et al. "Current state and prospects of edge computing within the Internet of Things (IoT) ecosystem." International Journal of Science and Research Archive 11.1 (2024): 1863-1873.
Edge Computing in B5G (MEC)
  Cao, Dun, et al. "Cost-effective task partial offloading and resource allocation for multi-vehicle and multi-MEC on B5G/6G edge networks." Ad Hoc Networks 156 (2024): 103438.
  Ibn‐Khedher, Hatem, et al. "6G‐edge support of Internet of Autonomous Vehicles: A survey." Transactions on Emerging Telecommunications Technologies 35.1 (2024): e4918.
Edge IoT Frameworks
  https://thin-edge.io/
  https://thingsboard.io/
  https://lfedge.org/
  https://www.edgexfoundry.org/
On task placement and edge offloading
  Mohammadi, Sudabeh, and Behzad Akbari. "Priority-Aware Resource Reallocation in Edge Computing Using Reinforcement Learning." Journal of Network and Systems Management 34.1 (2026): 20.
  Myyara, Marouane, et al. "Enhancing QoS for IoT Devices through Heuristics-based Computation Offloading in Multi-access Edge Computing." Infocommunications Journal 16.4 (2024).
  Moshiri, Parisa Fard, Murat Simsek, and Burak Kantarci. "On the interplay between network metrics and performance of mobile edge offloading." ICC 2024-IEEE International Conference on Communications. IEEE, 2024.
  Zhu, Feifan, et al. "Task offloading with LLM-enhanced multi-agent reinforcement learning in UAV-assisted edge computing." Sensors 25.1 (2024): 175.
References

## Slide 42
Questions and Discussion
?