## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 09

## Slide 2
What’s the Connection?
71, 89, 131, 151, 199, 241, 293, 307, 359, 367, 421, 433, 523, 587, 613, 739, 769, 823, 947, 983

## Slide 3
What’s the Connection?
71, 89, 131, 151, 199, 241, 293, 307, 359, 367, 421, 433, 523, 587, 613, 739, 769, 823, 947, 983
Prime Numbers

## Slide 4
What’s the Connection?
Tokyo
New Delhi
Cairo
Beijing
Buenos Aires

## Slide 5
What’s the Connection?
Tokyo
New Delhi
Cairo
Most populated world capitals
Beijing
Buenos Aires

## Slide 6
What’s the Connection?

## Slide 7
What’s the Connection?
Things that have 8 elements

## Slide 8
What’s the Connection?

## Slide 9
What’s the Connection?
Famous people died at 33 yo

## Slide 10
What’s the Connection?
A Piece of the Berlin Wall
Elvis Presley’s Hair
Lunch with Warren Buffett

## Slide 11
What’s the Connection?
A Piece of the Berlin Wall
Elvis Presley’s Hair
Lunch with Warren Buffett
Things sold on ebay for over 100K Dollars

## Slide 12
What’s the Connection?
The Hound of the Baskervilles
The Valley of Fear
A Study in Scarlet

## Slide 13
What’s the Connection?
The Hound of the Baskervilles
The Valley of Fear
A Study in Scarlet
Sherlock Holmes Stories

## Slide 14
What’s the Connection?

## Slide 15
What’s the Connection?
Animals have both male and female organs at the same time

## Slide 16
What’s the Connection?
Afghanistan
Burkina Faso
Ethiopia
Haiti
Senegal
Sierra Leone

## Slide 17
What’s the Connection?
Afghanistan
Burkina Faso
Ethiopia
Haiti
Senegal
Sierra Leone
Countries with adult literacy rates under 50 %

## Slide 18
What’s the Connection?

## Slide 19
What’s the Connection?
Blockbusters that resulted in losses at the box office

## Slide 20
What’s the Connection?

## Slide 21
What’s the Connection?
Foods and Drinks that were discovered accidentally

## Slide 22
What’s the Connection?

## Slide 23
What’s the Connection?
Fibonacci Patterns

## Slide 24
Μεταφορά Δεδομένων (IoT Networking)

## Slide 25
Networking in IoT: Definition
IoT Networking: Networking enables IoT devices (sensors, actuators, wearables, appliances) to transmit data to gateways, edge servers, or the cloud for monitoring, control and analytics.
Networking: The interconnection of devices and systems to exchange information using wired or wireless links
Multiple layers:
Device-to-device (local networks)
Device-to-gateway (edge networks)
Edge-to-cloud (wide-area networks)

## Slide 26
Networking in IoT: Motivation
IoT devices
  continuous streams of data
  to reach processing and storage points.
Proper networking enables:
  Real-time decision-making (latency-sensitive applications)
  Remote monitoring and control
  Scalable deployment across cities, factories, or homes
  Efficient resource utilization via edge or cloud processing
Networks are the backbone of IoT ecosystems
  Bottlenecks
  Delays
  Energy waste

## Slide 27
Networking in IoT: Challenges
Device Heterogeneity
Energy Constraints
Scalability
Latency
Reliability
Congestion
Security
Cost
Discussion

## Slide 28
Networking in IoT: Use-cases
Use Case | Devices | Network Technologies | Key Networking Requirements
Smart Home | Smart bulbs, thermostats, security cameras, plugs | Wi-Fi, BLE, Zigbee, Thread | Moderate latency, interoperability, low-power sensors
Smart City | Air quality sensors, street lights, parking meters | LoRaWAN, NB-IoT, LTE-M | Long range, low power, large-scale deployment
Industrial IoT | Robots, PLCs, machines, vibration sensors | Ethernet, Wi-Fi 6/6E, 5G URLLC, ProfiBus, Modbus | Ultra-low latency, deterministic communication, high throughput
Healthcare & Wearables | Heart-rate monitors, medical patches, infusion pumps | BLE, Wi-Fi, 5G | Reliability, mobility, ultra-low power for wearables
Smart Agriculture | Soil sensors, irrigation controllers, livestock tags | LoRa, NB-IoT, 4G/5G for drones | Long range, low power, tolerance to intermittent connectivity
Smart Transportation | Connected cars, GPS trackers, traffic sensors | 5G (eMBB/URLLC), LTE, DSRC/V2X | High mobility, low latency, reliable wide-area coverage
Smart Retail | RFID readers, smart shelves, inventory sensors | Wi-Fi, BLE, RFID, Ethernet | Medium mobility, moderate throughput, reliable indoor coverage
Energy Grid | Smart meters, substation sensors, grid controllers | PLC (Power Line Comm.), LTE-M, NB-IoT, Fiber | High reliability, long lifetime, secure and resilient communication

## Slide 29
IoT Device Networking
Edge Networking
Cloud Networking
Networking in IoT: End-to-end Layered Architecture
Sensing & Actuation
Aggregation, filtering, local analytics
Large-scale storage, batch analytics, ML training

## Slide 30
IoT Device Networking: Overview
This layer covers how IoT devices communicate:
  Device ↔ Device (intra-IoT exchanges)
  Device ↔ Gateway / Edge Node
Typically involves short-range or low-power networks optimized for:
  Limited battery
  Small data packets
  High device density
Gateways serve as aggregation points that translate local IoT networks into higher-capacity upstream networks.

## Slide 31
IoT Device Networking: Requirements
Low Power Consumption
  Many devices run on small batteries for months/years.
  Example: BLE sensors, LoRa environmental sensors.
Short-to-Medium Range Communication
  Typically within 10–100 m (Wi-Fi, BLE, Zigbee).
  Long-range exceptions: LPWAN (LoRaWAN, Sigfox).
Suitable Throughput
  Small payloads for sensors (few bytes/minute)
  High throughput for cameras (Wi-Fi or wired)
High Device Density Support
  E.g., 200+ sensors in a smart building.
Reliability & Robustness
  Must operate in interference-prone environments.
Cost Efficiency
  Cheap radios, simple antennas, easy deployment.

## Slide 32
IoT Device Networking: Network Technologies (1)
Technology | Type | Description | Specificities | Range | Data Rate | Power Consumption | Topology | Use Cases
Ethernet | Wired | High-speed LAN connection | Very reliable, low latency | Cable length | Up to Gbps | N/A (powered) | Star | Industrial machinery, hubs, fixed IoT
RS-485 / Modbus / Fieldbus | Wired | Industrial automation buses | Deterministic, noise-resistant | 100–1200 m | Low | N/A | Multi-drop | IIoT, factories, PLCs
Wi-Fi (2.4/5/6 GHz) | Wireless | High-bandwidth WLAN | Ubiquitous, easy integration | 20–50 m | High (100 Mbps–Gbps) | Medium to High | Star | Cameras, appliances, smart home
Bluetooth Low Energy (BLE) | Wireless | Ultra-low-power short-range link | Very low energy, simple pairing | 5–30 m | Low (1 Mbps) | Very Low | Star | Wearables, beacons

## Slide 33
IoT Device Networking: Network Technologies (2)
Technology | Type | Description | Specificities | Range | Data Rate | Power Consumption | Topology | Use Cases
Zigbee, Thread | Wireless | Low-power multi-hop mesh | Supports dense sensor networks | 10–100 m | Low (250 kbps) | Low | Mesh | Smart home sensors, automation
Z-Wave | Wireless | Low-power home automation | Sub-GHz band → low interference | 30–100 m | Low (100 kbps) | Low | Mesh | Smart home devices
LoRa, LoRaWAN | Wireless (LPWAN) | Long-range low-power WAN | Very long range, tiny payloads | 2–15 km | Very Low (0.3–50 kbps) | Very Low | Star (gateway) | Agriculture, remote sensors
Sigfox | Wireless (LPWAN) | Ultra-narrowband IoT | Very small messages, low cost | 5–20 km | Very Low (100 bps) | Very Low | Star | Asset tracking, metering

## Slide 34
IoT Device Networking: Wi-Fi Overview
Definition
  Wi-Fi (Wireless Fidelity) is a family of wireless networking technologies based on the IEEE 802.11 standards.
  It enables devices to exchange data wirelessly using radio waves in unlicensed frequency bands
    mainly 2.4 GHz and 5 GHz, with 6 GHz for Wi-Fi 6E/7
  Supports high data rates (from a few Mbps to several Gbps) and medium-range coverage (20–50 m indoors).
Relevance to IoT
  Ubiquity in homes, offices, universities.
  Good for high-bandwidth IoT devices (cameras, appliances, hubs).
  Wide vendor support, interoperability and ease of deployment.
  Not ideal for ultra-low-power sensors (BLE/Zigbee are better).
Core IEEE 802.11 Standards (Generations):
  802.11b/g/n → 2.4 GHz
  802.11a/n/ac → 5 GHz
  802.11ax (Wi-Fi 6/6E) → 2.4, 5, 6 GHz
  802.11be (Wi-Fi 7) → Multi-GHz, extremely high throughput

## Slide 35
IoT Device Networking: Wi-Fi Architecture
Basic Architecture Elements
  Access Point (AP)
    Provides wireless connectivity
    Acts as a bridge between Wi-Fi and wired network (LAN/WAN).
  Stations (STAs)
    Devices connected to the AP
    Sensors, laptops, cameras, IoT gateways
  Distribution System (DS)
    The wired or wireless backbone interconnecting multiple APs.
Operating Modes
  Infrastructure Mode (most common):
    Devices connect to an AP.
    AP connects to LAN and to the Internet.
    Used for homes, enterprise Wi-Fi, IoT gateways.
  Ad-Hoc Mode (IBSS):
    Devices communicate peer-to-peer without an AP.
    Rare for IoT (limited scalability).
Extended Architecture
  ESS (Extended Service Set)
    Multiple APs with the same SSID covering a large area.
    Enables roaming between APs
    Important for mobile IoT: robots, AGVs
  Mesh Wi-Fi
    APs connect wirelessly to each other (802.11s).
    Useful when wired backhaul is not available.

## Slide 36
IoT Device Networking: Wi-Fi Medium Access & Frames
Medium Access Control (MAC) = CSMA/CA protocol:
  Carrier Sense
    Device listens to see if channel is free.
  Collision Avoidance
    Devices wait random backoff before transmitting.
  Optional Request to Send/Clear to Send (RTS/CTS)
    Reduces hidden-node collisions.
  This makes Wi-Fi non-deterministic (important limitation for time-critical IoT)
Wi-Fi Frame Types (as per 802.11)
    Management frames → association, authentication, beacons
    Control frames → RTS/CTS, ACK
    Data frames → payload data
Association Steps
  Scan for APs (active or passive)
  Authentication
  Association
  DHCP for IP configuration
  Data transfer

## Slide 37
IoT Device Networking: Wi-Fi Protocols & Standards
Amendment | Description | Notes
802.11i | Security (WPA2) | AES-based encryption
802.11e | Quality of Service (QoS) | Priorities (voice, video, best-effort, background)
802.11n | MIMO, channel bonding | Big speed increase
802.11ac | 5 GHz only, MU-MIMO | High throughput
802.11ax (Wi-Fi 6) | OFDMA, uplink MU-MIMO | Improves dense IoT performance
802.11be (Wi-Fi 7) | 320 MHz channels, multi-link | Extreme throughput
Frequency Bands
  2.4 GHz → longer range, more interference
  5 GHz → higher speed, shorter range
  6 GHz (Wi-Fi 6E/7) → wide spectrum, low interference, high performance
Regulatory Bodies (for frequency rules)
  IEEE: technical standardization
  Wi-Fi Alliance: certification, interoperability
  ETSI (EU): spectrum regulation
  FCC (US): radio frequency regulation
https://standards.ieee.org/standard/802_11-2020.html
https://www.wi-fi.org/discover-wi-fi

## Slide 38
IoT Device Networking: Wi-Fi Evaluation (1)
Strengths
Limitations
Where Wi-Fi fits in IoT
Discussion

## Slide 39
IoT Device Networking: Wi-Fi Evaluation (2)
Strengths
  High bandwidth supports:
    Cameras
    Audio devices
    Smart appliances
    Gateways aggregating sensor data
  Ubiquitous, easy to configure.
  Mature, widely supported across devices.
Limitations
  Medium/high power consumption
    not suitable for tiny battery sensors.
  Congested 2.4 GHz band
    interference, collisions.
  Non-deterministic MAC
    not ideal for real-time industrial control.
  Limited coverage for outdoor IoT
Where Wi-Fi fits in IoT
  Smart home
  Edge gateways
  High-bandwidth industrial endpoints
  Wearables (occasionally, but BLE preferred)

## Slide 40
Edge Networking: Overview
Definition
  Networking between IoT gateways, local edge nodes and regional/mobile networks.
  Ensures that data from IoT devices can be aggregated, processed, and transmitted toward cloud or compute nodes located “close” to the user.
Edge nodes often perform:
  local filtering
  ML inference
  storage and caching
  offloading from IoT devices
Motivation = Move computation closer to data for:
  lower latency
  bandwidth savings
  reliability (fallback)
  security
Critical for real-time IoT workloads: robotics, autonomous vehicles, industrial systems.

## Slide 41
Edge Networking: Requirements
Low Latency
  ms-level communication needed
  robotic control, AR/VR, autonomous systems.
High Reliability - Determinism
  Predictable performance
  IIoT and smart grids.
High Throughput
  Streaming sensors, high-resolution cameras, edge inference workloads.
Mobility Support
  Vehicles, drones, AGVs in warehouses.
Scalability
  Many edge devices (robots, sensors, controllers).
Security & Isolation
  Network slicing, QoS, encryption, local policy enforcement.

## Slide 42
Edge Networking: Network Technologies
Technology | Type | Description | Specificities | Range | Data Rate | Power | Topology | Typical Use Cases
Ethernet (1G/10G/40G) | Wired | Primary edge backhaul | Very low latency, deterministic | N/A | Gbps–Tbps | N/A | Star | Edge servers, industrial gateways
Fiber (FTTx, DWDM) | Wired | High-speed backbone | Extremely high capacity | Kilometers | 10–400 Gbps | N/A | Point-to-point | Cloud ↔ Edge transport
Ethernet TSN | Wired | Time-sensitive networking | Guaranteed timing | meters–100 m | Gbps | N/A | Star | Industrial automation
Wi-Fi 6/6E | Wireless | High-throughput LAN | OFDMA for dense clients | 20–50 m | Up to Gbps | Medium | Star | Edge gateway uplinks
4G LTE | Wireless | Mobile broadband | Good coverage | km | 100 Mbps | Medium | Star | Mobile IoT, fallback
5G (NSA/SA) | Wireless | Latest mobile network | URLLC, network slicing | km | 1–20 Gbps | Medium | Star | Edge networks, MEC
Private LTE / Private 5G | Wireless | Dedicated industrial cellular | Very reliable, on-premise | km-scale | High | Medium | Star | Factories, ports, mining

## Slide 43
Edge Networking: 5G Overview
Definition
  5th generation cellular network standard defined by 3GPP.
  Supports massively heterogeneous devices: smartphones, IoT sensors, robots, vehicles.
  Designed to support edge computing, network slicing, and ultra-low latency workloads.
5G Performance Goals
  Enhanced Mobile Broadband (eMBB) = multi-Gbps speeds
  Massive Machine-Type Communications (mMTC) = millions of IoT devices per km²
  Ultra-Reliable Low-Latency Communications (URLLC) = sub-ms latency, high reliability
Frequency Spectrum
  Sub-6 GHz (FR1): wide coverage
  mmWave (FR2): extremely high throughput, short range
  Mid-band: best balance for edge applications

## Slide 44
Edge Networking: Simplified 5G Architecture (1)

## Slide 45
Edge Networking: Simplified 5G Architecture (2)
Core Components
  gNB (Next-Gen Base Station)
    Handles radio access, beamforming, scheduling.
  5G Core (5GC)
    AMF (Access Management)
    SMF (Session Management)
    UPF (User Plane Function) (key for edge computing)
  MEC Nodes (Multi-access Edge Computing)
    Placed at base stations or regional data centers
    host applications close to users.
Key Architectural Principles
  Service-Based Architecture (SBA)
    modular network functions via APIs
  Network Slicing
    logical networks with dedicated QoS
  Separation of Control Plane & User Plane (CUPS)
    data paths routed to nearest edge node

## Slide 46
Edge Networking: 5G Protocols & Standards
Radio Access (RAN) Protocols
  PHY – OFDM, modulation (QPSK, QAM)
  MAC – scheduling, HARQ
  RLC – error correction
  PDCP – ciphering, header compression
  RRC – connection setup & control
Core Network (5GC) Standards
  Defined by 3GPP Release 15, 16, 17, 18
    Rel 15 → initial 5G
    Rel 16 → URLLC, industrial IoT
    Rel 17 → NTN, low-power IoT improvements
    Rel 18 → 5G-Advanced (AI-native network, improvements)
  https://www.3gpp.org/5g
  https://www.etsi.org/technologies/multi-access-edge-computing

## Slide 47
Edge Networking: 5G Evaluation & Discussion (1)
Strengths
Limitations
Where 5G Is Best

## Slide 48
Edge Networking: 5G Evaluation & Discussion (2)
Strengths
  Low latency for robotic control, drones, AR/VR
  High throughput for cameras, AGVs, industrial gateways
  Massive device density for smart cities
  Mobility support for vehicles, logistics
  Network slicing & QoS for isolation and prioritization
  MEC for low-latency edge compute integration
Limitations
  High deployment cost (infrastructure, spectrum)
  mmWave coverage is limited indoors/outdoors
  Increased complexity (RAN + 5GC + slicing + MEC)
  Not ideal for ultra-low-power IoT (NB-IoT & LTE-M still relevant)
Where 5G Is Best
  Industry 4.0
  Autonomous vehicles
  Smart ports & logistics
  Smart manufacturing
  Large-scale video analytics

## Slide 49
Cloud Networking: Overview
Definition
  Cloud networking refers to the communication infrastructure that connects:
    Edge to Regional Data Centers
    Data Center to Data Center
    Intra-Data Center (rack to rack)
  It transports large volumes of IoT data for:
    ML training
    Data warehousing
    Federated aggregation
    Long-term storage
    Global analytics
IoT Motivation
  IoT generates massive continuous data streams.
  Requires high-throughput, low-latency, and high reliability.
  Needs scalability to handle millions of devices and TB/PB data volumes.
  Ensures global accessibility of data across distributed cloud environments.
Most Important Features
  High-bandwidth backbones
  Redundant & fault-tolerant paths
  Software-defined control (SDN)
  Multi-region connectivity
  Optical transport systems

## Slide 50
Cloud Networking: Requirements
Performance Requirements
  Ultra-high throughput (10–400 Gbps per link; up to multi-terabit aggregates)
  Low and predictable latency (microsecond-level in DCs)
  High reliability (redundancy, ECMP, BFD, optical protection switching)
Operational Requirements
  Scalability
    Millions of flows; elastic scaling of compute
  Security
    TLS/IPsec tunnels, VPC isolation, private subnets
  Programmability
    SDN controllers, programmable switches (P4)
Example Constraints
  ML training jobs require parallel high-speed, lossless transport
  Multi-cloud workloads need inter-DC optical backbone
  Large IoT networks need data ingestion pipelines (streaming, ETL)

## Slide 51
Cloud Networking: Network Technologies
Technology | Type | Description | Specificities | Range | Data Rate | Power | Topology | Use Cases
Ethernet (10/40/100/400G) | Wired | Standard data center networking | Low latency, cheap, scalable | <100 m (copper), <10 km (fiber) | 10–400 Gbps | N/A | Leaf–spine | DC internal networking
Fiber Optics (DWDM, OTN) | Wired | Long-haul optical backbone | Extremely high throughput | 10–1000 km | 100–400 Gbps (per lambda) | N/A | Mesh | Inter–data center transport
MPLS | Wired | Carrier-grade routing | Traffic engineering, VPNs | City/country | Multi-Gbps | N/A | Mesh | Cloud ↔ ISP connectivity
SD-WAN | Wired/Wireless | Software-defined WAN | Policy-based routing | Global | Varies | N/A | Overlay | Multi-cloud networks
Microwave Backhaul | Wireless | Point-to-point radio | Quick deploy; medium BW | 5–20 km | 1–2 Gbps | Medium | Point-to-point | Remote DC connections
Satellite (LEO) | Wireless | Space-based WAN | Global coverage | Global | 50–300 Mbps | Medium | Mesh | Remote cloud nodes

## Slide 52
Cloud Networking: Optical Networks Overview
Definition
  Networks that use light transmitted through optical fibers to carry data.
  They form the primary backbone of:
    Cloud providers (AWS, Azure, GCP)
    Telecom operators
    Inter-continental networks
Motivation
  Extremely high bandwidth (Tbps-class)
  Very low signal loss
  Immune to electromagnetic interference
  Long-distance transmission with few regenerators
Types of Optical Networking
  WDM (Wavelength Division Multiplexing) Multiple wavelengths (‘colors’) on a single fiber.
  DWDM (Dense WDM) 40–80+ channels, each 100–400 Gbps.
  CWDM (Coarse WDM) Cheaper, fewer channels.
  OTN (Optical Transport Network) Digital wrapper for wavelength services (error correction, framing).

## Slide 53
Cloud Networking: Optical Network Architecture (1)

## Slide 54
Cloud Networking: Optical Network Architecture (2)
Optical Transceivers
  Convert electrical ↔ optical signals
  Installed in switches, routers, and DWDM systems
  Common types: SFP/SFP+, QSFP/QSFP28, QSFP-DD, CFP
  Support speeds from 10G to 400G+
  Variants for distance and wavelength:
    LR/ER/ZR (long distance)
    CWDM/DWDM (specific wavelength channels)
Passive Optical Components
  WDM Mux/DeMux: combine/separate wavelengths on one fiber, no power needed
  Splitters & Couplers: divide optical power into multiple paths, used in PONs
  Patch panels and splice trays: fiber organization and termination
  Optical connectors (LC, SC, MPO): physical fiber interfaces
ROADMs (Reconfigurable Optical Add-Drop Multiplexers)
  Dynamically route and switch wavelengths without electrical conversion
  Enable programmable optical paths
  Features:
    Colorless: any wavelength
    Directionless: any path
    Contentionless: no conflicts

## Slide 55
Cloud Networking: Optical Network Architecture (3)
Optical Amplifiers
  Boost optical signal strength without electrical conversion
  Extend long-haul transmission distance
  Main types:
    EDFA (Erbium-Doped Fiber Amplifier)
    Raman Amplifier (distributed amplification)
Optical Transport Switches / OTN Equipment
  Implement OTN (G.709) framing and multiplexing
  Groom and aggregate multiple optical circuits
  Provide monitoring, FEC, error detection
  Act as switching fabric for cloud/carrier networks
Packet–Optical Integration Devices
  Combine Ethernet switching, OTN, and WDM in one system
  Enable efficient metro and DC interconnections
  Useful for high-volume IoT and edge-to-cloud traffic

## Slide 56
Cloud Networking: Optical Networks Protocols & Standards
Transmission Standards
  ITU-T G.652 / G.655 / G.657 – fiber types
  ITU-T G.709 (OTN) – framing, multiplexing
  IEEE 802.3bs / 802.3cu – 200G/400G Ethernet
Control & Management
  SDN controllers for optical switching
  GMPLS – control plane for optical networks
  NETCONF/YANG – configuration APIs
Transport Protocols Over Optical Paths
  Ethernet
  MPLS
  IPv6
  VXLAN/EVPN overlays
https://www.itu.int/rec/T-REC-G/en
https://standards.ieee.org/broadcom/ethernet.html

## Slide 57
Cloud Networking: Optical Networks Evaluation & Discussion (1)
Strengths
Limitations
Best Application Scenarios

## Slide 58
Cloud Networking: Optical Networks Evaluation & Discussion (2)
Strengths
  Highest bandwidth available (100–800 Gbps per wavelength)
  Long-haul capability (100s–1000s km)
  Ultra-low latency (speed of light in fiber ~5 μs/km)
  Highly reliable (redundancy, automatic protection switching)
  Ideal for multi-region IoT data transport
Limitations
  Very high installation cost
  Requires physical fiber routes
  Long deployment time
  Active components require maintenance
Best Application Scenarios
  Cloud–cloud backbone
  Cloud–edge regional links
  High-volume IoT analytics pipelines
  Machine learning data transport
  Long-haul intercontinental links (subsea cables)

## Slide 59
References
Pahlavan, K., & Krishnamurthy, P. (2021). Evolution and impact of Wi-Fi technology and applications: A historical perspective. International Journal of Wireless Information Networks, 28(1), 3-19.
Reshef, E., & Cordeiro, C. (2022). Future directions for Wi-Fi 8 and beyond. IEEE Communications Magazine, 60(10), 50-55.
Kane, L., Liu, V., McKague, M., & Walker, G. (2023). An Experimental Field Comparison of Wi-Fi HaLow and LoRa for the Smart Grid. Sensors, 23(17), 7409.
Meftah, E. H., Benmahmoud, S., & Rabehi, A. (2024, December). Innovative Wireless Solutions for Real-Time ECG Monitoring: Leveraging BLE, Wi-Fi, and LoRa Technologies. In 2024 International Conference on Telecommunications and Intelligent Systems (ICTIS) (pp. 1-6). IEEE.
Mahmood, A., Beltramelli, L., Abedin, S. F., Zeb, S., Mowla, N. I., Hassan, S. A., ... & Gidlund, M. (2021). Industrial IoT in 5G-and-beyond networks: Vision, architecture, and design trends. IEEE Transactions on Industrial Informatics, 18(6), 4122-4137.
Salahdine, F., Han, T., & Zhang, N. (2023). 5G, 6G, and Beyond: Recent advances and future challenges. Annals of Telecommunications, 78(9), 525-549.
Sufyan, A., Khan, K. B., Khashan, O. A., Mir, T., & Mir, U. (2023). From 5G to beyond 5G: A comprehensive survey of wireless network evolution, challenges, and promising technologies. Electronics, 12(10), 2200.
Khan, B. S., Jangsher, S., Ahmed, A., & Al-Dweik, A. (2022). URLLC and eMBB in 5G industrial IoT: A survey. IEEE Open Journal of the Communications Society, 3, 1134-1163.
Shah, J. H. (2022). 5G-Enabled IoT Mesh for Real-Time Control and Predictive Maintenance. International Journal of Scientific Research in Computer Science, Engineering and Information Technology, 593-605.
https://www.3gpp.org/technologies/5g-system-overview
https://www.nokia.com/mobile-networks/ran/anyran/open-ran/open-ran-explained/
https://www.etsi.org/technologies/multi-access-edge-computing
Yoo, S. B. (2021). Prospects and challenges of photonic switching in data centers and computing systems. Journal of Lightwave Technology, 40(8), 2214-2243.
Kogan, S. S. (2025). Fiber optic solutions for data centres with packet interfaces based on Ethernet. Part 4. Standardized coherent solutions for data center interconnect (DCI) networks. Last Mile, (5), 58-68.
Li, W., Yuan, G., Wang, Z., Tan, G., Zhang, P., & Rouskas, G. N. (2024). Fast and scalable all-optical network architecture for distributed deep learning. Journal of Optical Communications and Networking, 16(3), 342-357.

## Slide 60
Questions and Discussion
?