## Slide 1
Διαδίκτυο των Πραγμάτων (ΔτΠ)
Διάλεξη 10

## Slide 2
Who is the thief?

## Slide 3
Who is the thief?

## Slide 4
Who is the thief?

## Slide 5
Who is the thief?

## Slide 6
Who is the thief?

## Slide 7
Who is the thief?

## Slide 8
Who is the thief?

## Slide 9
Who is the thief?

## Slide 10
Who is the thief?

## Slide 11
Who is the thief?

## Slide 12
Θέματα Ασφαλείας στο ΔτΠ
(IoT Security)

## Slide 13
IoT Security: Definition
IoT Security: The application of cyber-security principles to IoT systems, focusing on protecting resource-constrained, physically exposed devices, their communications and edge/cloud services across the entire IoT architecture.
Cyber-Security: The practice of protecting computer systems, networks and digital data from unauthorized access, attacks, damage, or disruption, in order to ensure confidentiality, integrity and availability.

## Slide 14
IoT Security: Motivation & Challenges
Resource Constraints
Massive Scale
Device Heterogeneity
Physical Exposure
Long Device Lifetime
Update & Patching
Data sensitivity
Multi-domain
Device Mobility
Regulatory/Legal
IoT security is cyber-security on steroids.

## Slide 15
IoT Security: Basic Terms
Term | Definition | Example in the IoT domain
Authentication (AuthN) | Verifying the identity of a device or user | IoT camera logging in with a certificate to a cloud server
Authorization (AuthZ) | Controlling access to resources based on identity | MQTT broker allowing only certain devices to publish to specific topics
Confidentiality | Protecting data from unauthorized access | Encrypting sensor readings sent over WiFi or LoRa
Integrity | Ensuring data is accurate and unaltered | Using message authentication codes (MACs) to detect tampered sensor data
Availability | Ensuring systems and data are accessible when needed | Edge gateway remains online to collect data from sensors
Privacy | Protecting personal or sensitive information | Smart thermostat anonymizing household usage data before sending to cloud
Non-repudiation | Preventing entities from denying their actions | Signed firmware update ensures vendor cannot deny it was issued
Accountability (Auditing) | Tracking actions and detecting misuse | Logging device commands in a central IoT management dashboard

## Slide 16
IoT Security: CIA Triad
A foundational model in cybersecurity defining three core security objectives:
  Confidentiality
  Integrity
  Availability.
Introduced:
  Early 1970s by James Anderson
  Computer security for government and military systems.
Confidentiality: Protects data from unauthorized disclosure (e.g., encryption at rest and in transit).
Integrity: Ensures data and system state are accurate and unaltered (e.g., digital signatures, MACs, hashes).
Availability: Keeps systems and services operational and accessible (e.g., redundancy, fault-tolerant networks).

## Slide 17
IoT Security: A layered approach
Layer | Name | Main Function
7 | Application | Provides network services to users
6 | Presentation | Data formatting, encryption
5 | Session | Manages sessions & connections
4 | Transport | Reliable or fast data delivery
3 | Network | Data routing
2 | Data Link | Data framing, MAC address handling
1 | Physical | Raw bit transmission
IoT
Device Layer
Sensors, actuators, and microcontrollers. Focus on secure boot, firmware integrity and physical security.
Network Layer
Communication protocols (MQTT, CoAP, BLE, WiFi, 5G). Focus on encryption, authentication and network segmentation.
Edge Layer
Local aggregation and processing. Focus on container isolation, OS hardening and secure updates.
Cloud & Applications Layer
Device management, dashboards, analytics. Focus on identity management, access control, logging, and monitoring.

## Slide 18
IoT Threat Modelling: Definition
Threat Modelling: A systematic cyber-security process to identify, analyze and mitigate potential threats to a system before they can be exploited.
Purpose:
  Understand the attack surface and system vulnerabilities.
  Prioritize security measures based on risk.
  Guide design decisions and architecture for secure systems.
For IoT:
  IoT systems are distributed, heterogeneous and resource-constrained.
  Security failures can have physical consequences (sensors, actuators, critical infrastructure).
  Helps engineers anticipate attacks before deployment, reducing expensive fixes later.

## Slide 19
IoT Threat Modelling: Basic Concepts (1)
Term | Definition | IoT Example
Asset | Valuable system component or data that needs protection | IoT Physical device, Sensor readings, actuator commands, cloud database
Threat | Potential cause of unwanted impact or harm | Unauthorized access to smart thermostat settings
Vulnerability | Weakness in a system that can be exploited | Default password on IoT camera, unpatched firmware
Attack | Action taken to exploit a vulnerability | Brute-force login on an MQTT broker
Attack Surface | All points where an attacker can try to enter or affect a system | Open ports, exposed APIs, wireless interfaces of IoT devices
Risk | Likelihood × impact of a threat exploiting a vulnerability | High risk if a compromised sensor can shut down a water pump
Mitigation (Control) | Measures to reduce risk | TLS encryption for MQTT, secure boot, firmware signing
Threat Actor (Attacker) | Entity capable of carrying out an attack | Hacker, insider, malicious firmware provider

## Slide 20
IoT Threat Modelling: Basic Concepts (2)
Term | Definition | IoT Example
Trust Boundary | A point where trust assumptions change within the system | Between edge gateway and cloud service
Entry Point | Where an attacker can attempt access or influence | WiFi interface, Bluetooth connection, physical port on sensor
Impact | Consequence if a threat materializes | Data leak, actuator malfunction, service downtime
Likelihood (Probability) | Chance that a threat will exploit a vulnerability | High likelihood if devices have default credentials
Security Requirement | Necessary measure to protect an asset | Require mutual authentication for device-to-cloud communication
Residual Risk | Risk remaining after mitigation | Small chance of firmware tampering despite signed updates
Security Policy | Rules that govern allowed behaviors | Devices must authenticate before publishing data
Threat Scenario | Combination of actor, asset, vulnerability, and attack leading to risk | Hacker exploiting default MQTT credentials to turn on smart lights

## Slide 21
IoT Threat Modelling: Frameworks (1)
STRIDE
  Description:
    Developed by Microsoft, early 1990s
    Structured approach to identify security threats during system design
  Operation / Functionality:
    Categorizes threats into six types: Spoofing, Tampering, Repudiation, Information Disclosure, Denial of Service, Elevation of Privilege
    Helps map threats to assets systematically
  Relevance to IoT:
    Applies at all IoT layers (devices, network, edge, cloud)
    Provides clear taxonomy for analyzing IoT-specific threats
    Example: Spoofing → rogue sensor, Tampering → modified actuator data
DREAD
  Description:
    Developed by Microsoft, 2000s
    Risk assessment framework to quantify and prioritize threats
  Operation / Functionality:
    Evaluates threats using five factors: Damage, Reproducibility, Exploitability, Affected users, Discoverability
    Assigns numeric scores to prioritize mitigations
  Relevance to IoT:
    Helps prioritize security measures for resource-constrained IoT devices
    Example: Decide which sensors or gateways to secure first

## Slide 22
IoT Threat Modelling: Frameworks (2)
MITRE ATT&CK for IoT
  Description:
    Developed by MITRE, continuously updated
    Knowledge base of real-world attacker tactics, techniques, and procedures (TTPs)
  Operation:
    Maps attacker behaviors to IoT-specific attack vectors
    Helps simulate attacks or perform red-teaming
  Relevance to IoT:
    Provides practical examples of IoT attacks
    Useful for defense testing and threat anticipation
NIST IoT Risk Framework
  Description:
    Developed by NIST, 2019
    Guidelines for IoT risk management and assessment
  Operation:
    Structured methodology: identify risks, assess likelihood, apply controls
    Considers device lifecycle, supply chain and operational environment
  Relevance to IoT:
    Tailored for large-scale IoT deployments
    Helps plan mitigations across devices, edge and cloud

## Slide 23
IoT Threat Modelling: Major Attack Classes
Attack Class | Explanation | IoT Example
Denial of Service (DoS/ DDoS) | Overwhelming a device, network, or service to make it unavailable | Botnet flooding smart home gateway or cloud API, preventing sensor updates
Man-in-the-Middle (MITM) | Intercepting and potentially modifying communication between devices (ACTIVE/PASSIVE) | Sniffing MQTT traffic between a sensor and broker on unencrypted WiFi
Spoofing (Identity Theft) | Impersonating a legitimate device or user to gain access | Rogue sensor pretending to be a temperature sensor to send false readings
Tampering | Modifying hardware, firmware, or data to disrupt operation | Modifying smart meter firmware to report false energy usage
Eavesdropping (Information Disclosure) | Unauthorized access to sensitive data (PASSIVE) | Capturing unencrypted BLE signals from wearable health devices
Replay Attack | Resending captured messages to trick the system | Replaying actuator commands to open a smart lock repeatedly
Privilege Escalation | Gaining higher access than intended | Exploiting a vulnerability in an IoT gateway to gain admin rights
Firmware & Software Exploits | Exploiting vulnerabilities in firmware or software | Exploiting buffer overflow in a connected camera’s firmware to take control
Physical Attacks | Direct tampering with hardware or storage | Stealing a smart lock and extracting keys from its memory
Injection Attacks | Sending malicious input to manipulate device behavior | Injecting malformed MQTT payload to crash a sensor or gateway
Data Integrity Attacks | Manipulating sensor data to cause wrong decisions | Changing temperature readings to trigger false alarms in a smart HVAC system
Phishing and Social Engineering | Tricking users to gain access to IoT devices or credentials | Email or app-based attack convincing a user to reveal smart home login credentials
Cross-Site and API Attacks | Exploiting web interfaces or APIs controlling IoT devices | Exploiting weak REST API authentication on smart bulbs to turn them on/off remotely

## Slide 24
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?

## Slide 25
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials

## Slide 26
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials
Mobile app ↔ Pi; Mobile app ↔ Cloud; Pi ↔ Heater (physical interface)

## Slide 27
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials
Mobile app ↔ Pi; Mobile app ↔ Cloud; Pi ↔ Heater (physical interface)
Remote hacker (turn heater on/off, steal user data), local attacker (tamper with Pi or heater), malware on mobile app (disrupt system)

## Slide 28
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials
Mobile app ↔ Pi; Mobile app ↔ Cloud; Pi ↔ Heater (physical interface)
Remote hacker (turn heater on/off, steal user data), local attacker (tamper with Pi or heater), malware on mobile app (disrupt system)
WiFi interception (MITM), default credentials on Pi, unsecured API endpoints, malicious firmware update to Pi

## Slide 29
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials
Mobile app ↔ Pi; Mobile app ↔ Cloud; Pi ↔ Heater (physical interface)
Remote hacker (turn heater on/off, steal user data), local attacker (tamper with Pi or heater), malware on mobile app (disrupt system)
WiFi interception (MITM), default credentials on Pi, unsecured API endpoints, malicious firmware update to Pi
Unauthorized heater activation (fire hazard), privacy breach of usage patterns, device malfunction (heating failure)

## Slide 30
IoT Threat Modelling: Example
System Description:
Device: Raspberry Pi with:
  Temperature sensor embedded
  Actuator controlling a single smart heating device (via wired connection)
Mobile App: Controls the Pi via WiFi
Edge/Cloud Infrastructure: Stores user preferences, logs and schedules, accessed by mobile app over WiFi
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Mitigation
What needs protection?
Where does trust change?
Who could attack and why?
How could attackers exploit vulnerabilities?
What could go wrong?
How to reduce risk?
Raspberry Pi device, temperature sensor readings, actuator control signals, user data (preferences, schedules), mobile app credentials
Mobile app ↔ Pi; Mobile app ↔ Cloud; Pi ↔ Heater (physical interface)
Remote hacker (turn heater on/off, steal user data), local attacker (tamper with Pi or heater), malware on mobile app (disrupt system)
WiFi interception (MITM), default credentials on Pi, unsecured API endpoints, malicious firmware update to Pi
Unauthorized heater activation (fire hazard), privacy breach of usage patterns, device malfunction (heating failure)
Strong authentication (Pi & mobile), encrypted communication (TLS/DTLS), signed firmware updates, network segmentation, local monitoring/logging

## Slide 31
IoT Device-Layer Security: Overview
Layer Security Description:
  Ensures IoT devices themselves are secure against physical and logical attacks.
  Critical because devices are often physically exposed, resource-constrained and widely deployed.
Includes:
  Hardware Security: Trusted execution environments, secure elements, physical tamper resistance
  Firmware & Software Security: Secure boot, signed firmware, OS hardening
  Device Identity & Authentication: Unique IDs, certificates, cryptographic keys
  Access Control & Local Policies: Permissions on sensors/actuators, local authentication
Common Attacks:
  Physical tampering & theft
  Firmware exploits & backdoors
  Device spoofing & unauthorized access
  Side-channel attacks
Examples:
  Smart meters being physically opened to extract keys
  Raspberry Pi controlling a heater with default credentials exploited
  Sensors sending falsified readings due to tampered firmware

## Slide 32
IoT Device-Layer Security: Main Technologies
Tool | Type | Functionality | IoT Example
Secure Boot | Mechanism | Ensures only authenticated firmware runs on device | Raspberry Pi checks firmware signature before running
Trusted Platform Module (TPM) | Hardware | Stores cryptographic keys securely, supports device authentication | Smart home controller storing device keys securely
Hardware Security Module (HSM) | Hardware | Secure key storage & cryptographic operations | Industrial IoT sensor authenticating to edge gateway
Device Certificates & PKI (Public Key Infrastructure) | Protocol & Mechanism | Strong identity and authentication | IoT camera authenticating to cloud via TLS certificate
Firmware Signing & Verification | Mechanism | Protects against malicious firmware updates | OTA update for smart thermostat verified before install
Secure Elements (SE) | Hardware | Tamper-resistant storage for keys and secrets | Wearable health sensor storing keys inside SE
Local Access Control | Mechanism & Policy | Limits local access to device functions | Raspberry Pi actuator controlled only by authenticated app
Anti-Tamper Sensors | Hardware | Detect physical intrusion attempts | Industrial sensor triggers alert if casing opened

## Slide 33
IoT Network-Layer Security: Overview
Layer Security Description:
  Focuses on protecting data as it travels between IoT devices, gateways/edge nodes and cloud services.
  Prevents interception, tampering and unauthorized access over wireless and wired networks.
  Critical because IoT networks are heterogeneous, resource-constrained and often exposed.
Includes:
  Network Protocol Security: MQTT, CoAP, HTTP(S), AMQP
  Encryption & Confidentiality: TLS, DTLS, IPSec
  Authentication & Authorization: Device identity, API keys, OAuth
  Network Segmentation & Isolation: VLANs, firewalls, micro-segmentation
  Intrusion Detection & Monitoring: NIDS/NIPS adapted for IoT
Common Attacks Relevant to This Layer:
  Man-in-the-Middle (MITM) attacks
  Eavesdropping, sniffing sensitive data
  Replay attacks
  Denial of Service (DoS), flooding
  Rogue devices joining the network
Examples:
  MITM attack on MQTT broker over unencrypted WiFi
  IoT camera credentials sniffed on public WiFi
  DoS attack on smart light network preventing control via mobile app

## Slide 34
IoT Network-Layer Security: Main Technologies
Tool | Type | Functionality | IoT Example
TLS and DTLS | Protocol | Encrypts data in transit; ensures authentication | Secure MQTT communication from sensor to broker
IPSec | Protocol | Encrypts and authenticates IP traffic | Edge node VPN for industrial IoT devices
VPN (Virtual Networks) | Mechanism | Isolates traffic between devices and cloud | Raspberry Pi connecting to cloud via VPN
Network Access Control (NAC) | Mechanism | Ensures only authorized devices connect | IoT gateway allowing only registered sensors
Firewalls and ACLs | Mechanism | Controls network traffic flow | Home router firewall preventing external IoT access
OAuth 2.0 and API Keys | Protocol, Mechanism | Authorization and access control for APIs | Mobile app controlling smart heater securely via cloud API
Intrusion Detection & Prevention Systems (NIDS/NIPS) | Tool | Monitors network traffic for attacks | Detecting scanning or abnormal traffic from compromised IoT devices
Segmentation, VLANs, Micro-Segmentation | Mechanism | Limits exposure of IoT devices to threats | Isolating smart cameras from home WiFi for laptops

## Slide 35
IoT Edge-Layer Security: Overview
Layer Security Description:
  Protects intermediate nodes that aggregate, preprocess, or route data between IoT devices and cloud services.
  Critical because gateways/edge nodes often handle multiple devices, store sensitive data temporarily and perform computation, making them attractive targets.
Includes:
  Device-to-Edge Authentication: Securely verify devices connecting to gateway/edge node
  Data Preprocessing & Filtering Security: Ensure processed data is not tampered
  Container and Application Isolation: Run multiple services safely (e.g., via Docker)
  Firmware, OS Hardening: Secure software stack and updates on edge devices
  Monitoring & Logging: Detect anomalies, misbehavior, and attacks
Common Attacks Relevant to This Layer:
  Compromise of gateway to control downstream devices
  Injection of malicious data or commands
  Lateral movement attacks within network
  Firmware exploits or privilege escalation
  Data leakage to unauthorized parties
Examples:
  Raspberry Pi gateway compromised to manipulate multiple connected sensors
  Edge device running Docker containers; attacker escapes container to access system
  IoT gateway storing user data locally gets stolen

## Slide 36
IoT Edge-Layer Security: Main Technologies
Tool | Type | Functionality | IoT Example
Docker, Containerization | Tool & Mechanism | Isolates applications/services on edge devices | Edge node running sensor data preprocessing securely
Secure Boot, Firmware Signing | Mechanism | Prevents execution of unauthorized firmware | Signed OS image for Raspberry Pi gateway
OS Hardening | Mechanism & Practice | Reduce attack surface by disabling unnecessary services | Lightweight hardened Linux for IoT gateway
Device-to-Edge Authentication | Protocol & Mechanism | Authenticate IoT devices connecting to gateway | TLS client certificate for smart heater connecting to Raspberry Pi
Encrypted Local Storage | Mechanism | Protect data cached or temporarily stored | Edge node storing sensor readings in encrypted DB
Monitoring & Logging Tools | Tool | Detect anomalies, attacks, or misconfigurations | ELK stack for logging IoT edge activity
Access Control Policies | Mechanism | Restrict which processes or users can access resources | Only authorized apps can write to actuator control service
Virtualization, MicroVMs | Tool & Mechanism | Additional isolation for critical services | Running AI inference in Firecracker microVM on edge

## Slide 37
IoT Cloud & Application-Layer Security: Overview
Layer Security Description:
  Protects cloud services, IoT applications, and user-facing interfaces that process, store, and analyze IoT data.
  Critical because cloud services are central points for data aggregation and control, making them attractive targets for attacks.
Includes:
  Authentication & Authorization: Identity management for devices, apps, and users
  Data Protection: Encryption at rest and in transit, access policies
  API Security: Secure REST/GraphQL APIs, input validation, rate limiting
  Application & Service Hardening: Secure coding, patch management, runtime protection
  Monitoring, Logging & Incident Response: Detect anomalies, respond to threats, auditing
Common Attacks:
  Compromise of cloud accounts or APIs
  Data breaches and privacy violations
  Injection attacks (SQL, NoSQL, API misuse)
  Unauthorized remote control of IoT devices
  Insider threats or misconfigured permissions
Examples:
  Attacker exploits weak cloud API authentication to control smart heater remotely
  Data leak of user preferences or IoT sensor readings from cloud storage
  Malicious API request flooding cloud service causing denial-of-service

## Slide 38
IoT Cloud & Application-Layer Security: Main Technologies
Tool | Type | Functionality | IoT Example
TLS, HTTPS | Protocol | Encrypts data in transit | Mobile app sends commands to cloud over HTTPS
OAuth 2.0, OpenID Connect | Protocol | Authentication & authorization for apps and devices | Users authenticate to smart home cloud platform
Cloud IAM (Identity & Access Management) | Tool, Mechanism | Role-based access control for users and devices | AWS IoT IAM policies restricting access to device data
Encryption at Rest (AES, KMS) | Mechanism | Protects stored data | Sensor readings stored encrypted in cloud database
API Gateways, Throttling | Tool, Mechanism | Protect APIs, prevent abuse, input validation | Protect cloud IoT endpoints from excessive requests or injection attacks
Logging & Monitoring Tools | Tool | Audit access and detect anomalies | CloudWatch / ELK stack monitoring IoT cloud services
Secure Software Development Lifecycle (SSDLC) | Practice | Ensures apps are developed with security in mind | Code review, testing, vulnerability scanning for cloud apps
Intrusion Detection, Anomaly Detection | Tool | Detect malicious behavior in cloud services | Detect unusual command patterns sent to IoT devices

## Slide 39
Group Exercise: Design of Smart Factory Security System
Rasp Pis
Sensors (Temperature, Light, Vibration)
Actuators (Smart Heater, Industrial Fan)
Rasp Pis
WiFi
Serial
Factory Edge Server (Gateway)
ETH
ETH
City-level Cloud Data Centre
5G
Smart Factory Setup
  Sensors
    3 types (Temperature, Vibration, Light)
    Each sensor connects via WiFi to its respective Raspberry Pi.
    Short-distance communication
  Actuators
    2 types (Smart Heater, Industrial Fan)
    Connected to their respective Raspberry Pi via wired connection (serial).
      Higher reliability
      Lower latency
      Safety-critical control
  Processing Units
    Raspberry Pi per sensor actuator aggregation
  Factory Gateway/Edge Server:
    All Pis connected via wired Ethernet to a single factory-level edge server
  Cloud Infrastructure:
    Edge server sends aggregated data to city-level cloud via 5G network
Factory Edge Server (Gateway)
Factory Edge Server (Gateway)
5G
5G
Smart Factory 1
Smart Factory 2
Smart Factory N

## Slide 40
Group Exercise: Design of Smart Factory Security System
Rasp Pis
Sensors (Temperature, Light, Vibration)
Actuators (Smart Heater, Industrial Fan)
Rasp Pis
WiFi
Serial
Factory Edge Server (Gateway)
ETH
ETH
City-level Cloud Data Centre
5G
Factory Edge Server (Gateway)
Factory Edge Server (Gateway)
5G
5G
Smart Factory 1
Smart Factory 2
Smart Factory N
Current Security State:
  No security applied: default credentials, unencrypted WiFi, open APIs
Decision Criteria:
  Security: Does the mechanism effectively protect the system?
  Criticality: Is the asset important enough to justify protection?
  Performance: What is the latency/resource cost of applying this mechanism?
  Scalability: How well does it work as the system grows?
Instructions:
  Each layer has 4 mechanisms
  choose Yes or No for each.
  Justify choices based on trade-offs, criticality and practicality.

## Slide 41
Group Exercise: Design of Smart Factory Security System
Layer 1: Device-Level Security (Sensors + Actuators + Pis)
Mechanism/ Technology | Functionality | Recommended | Notes
Secure Boot | Only trusted firmware runs |  | 
TPM/ Secure Element | Stores keys securely |  | 
Physical Tamper Sensors | Detect device tampering |  | 
Firmware Signing | OTA updates verified |  | 

## Slide 42
Group Exercise: Design of Smart Factory Security System
Mechanism/ Technology | Functionality | Recommended | Notes
Secure Boot | Only trusted firmware runs | Yes | Critical for Pis/actuators; minimal performance cost
TPM/ Secure Element | Stores keys securely | No | Optional; cost may not justify for small setup
Physical Tamper Sensors | Detect device tampering | No | Not critical in this scenario
Firmware Signing | OTA updates verified | Yes | Avoids malicious firmware; important for actuators
Layer 1: Device-Level Security (Sensors + Actuators + Pis)

## Slide 43
Group Exercise: Design of Smart Factory Security System
Layer 2: Network-Level Security
Mechanism/Technology | Functionality | Recommended | Notes
WiFi WPA3 | Encrypts wireless sensor traffic |  | 
TLS/DTLS | Encrypts data in transit |  | 
VPN | Encrypted tunnel Edge → Cloud |  | 
Open WiFi/No Security | Unprotected traffic |  | 

## Slide 44
Group Exercise: Design of Smart Factory Security System
Layer 2: Network-Level Security
Mechanism/Technology | Functionality | Recommended | Notes
WiFi WPA3 | Encrypts wireless sensor traffic | Yes | Strong protection for sensor → Pi communication
TLS/DTLS | Encrypts data in transit | Yes | Secures Pi → gateway/cloud messages
VPN | Encrypted tunnel Edge → Cloud | No | Adds latency; optional if TLS used
Open WiFi/No Security | Unprotected traffic | No | High risk; should never be used

## Slide 45
Group Exercise: Design of Smart Factory Security System
Layer 3: Edge & Gateway Security
Mechanism/Technology | Functionality | Recommended | Notes
Local Logging/ Monitoring | Tracks events/anomalies |  | 
Remote Access Tools Open | Exposed RDP/SSH |  | 
Docker/Containerization | Isolates services |  | 
OS Hardening | Reduces attack surface |  | 

## Slide 46
Group Exercise: Design of Smart Factory Security System
Layer 3: Edge & Gateway Security
Mechanism/Technology | Functionality | Recommended | Notes
Local Logging/ Monitoring | Tracks events/anomalies | No | Optional for small deployments
Remote Access Tools Open | Exposed RDP/SSH | No | High risk; not required for basic setup
Docker/Containerization | Isolates services | Yes | Protects preprocessing tasks and analytics
OS Hardening | Reduces attack surface | Yes | Disables unused ports/services; minimal overhead

## Slide 47
Group Exercise: Design of Smart Factory Security System
Layer 4: Cloud & Application Security
Mechanism/Technology | Functionality | Recommended | Notes
TLS / HTTPS | Encrypts cloud communication |  | 
API Gateway/Rate Limiting | Protects cloud APIs |  | 
OAuth2 / OpenID Connect | Authentication & authorization |  | 
Logging/Monitoring/IDS | Detects anomalies |  | 

## Slide 48
Group Exercise: Design of Smart Factory Security System
Layer 4: Cloud & Application Security
Mechanism/Technology | Functionality | Recommended | Notes
TLS / HTTPS | Encrypts cloud communication | Yes | Essential for edge → cloud data
API Gateway/Rate Limiting | Protects cloud APIs | No | Optional for low traffic; important at scale
OAuth2 / OpenID Connect | Authentication & authorization | Yes | Prevents unauthorized cloud access
Logging/Monitoring/IDS | Detects anomalies | No | Optional for small setup; critical for multi-factory

## Slide 49
References
Threat Modelling in IoT
  Granata, Daniele, and Massimiliano Rak. "Systematic analysis of automated threat modelling techniques: Comparison of open-source tools." Software quality journal 32.1 (2024): 125-161.
  Salayma, Marwa. "Threat modelling in Internet of Things (IoT) environments using dynamic attack graphs." Frontiers in the Internet of Things 3 (2024): 1306465.
  He, Sizhe, et al. "Cascading failure in cyber–physical systems: A review on failure modeling and vulnerability analysis." IEEE Transactions on Cybernetics 54.12 (2024): 7936-7954.
Device Security
  Kumar, Sunil, et al. "A review of lightweight security and privacy for resource-constrained IoT devices." Computers, Materials and Continua 78.1 (2024): 31-63.
  Li, X., Wei, Q., Wu, Z., Guo, W., & He, L. (2024). Harden-IoT: hardening the EoL devices by intercepting the attack vector for future B5G/6G IoT. Wireless Networks, 30(8), 6797-6808.
Network Security
  Afzal, F., Uzair, A., Javed, M. A., & Naqvi, S. A. A. (2024). An Enhanced Approach for Wi-Fi Security and Authentication Protocols: A Systematic Approach towards WEP, WPA, WPA2, and WPA3. Spectrum of Engineering Sciences, 2(5), 379-403.
  Ji, Sharma, and Abhishek Kumar Mishra. "5g security issues challenges and solutions against ddos attacks: A survey." 2024 2nd International Conference on Disruptive Technologies (ICDT). IEEE, 2024.
  Abderrahmane, Tamali, Amardjia Nourredine, and Tamali Mohammed. "Experimental analysis for comparison of wireless transmission technologies: Wi-Fi, Bluetooth, ZigBee and LoRa for mobile multi-robot in hostile sites." Int. J. Electr. Comput. Eng.(IJECE) 14.3 (2024): 2753-2761.
Edge/Cloud & App Security
  Shahid, Jahanzeb, et al. "A comparative study of web application security parameters: Current trends and future directions." Applied Sciences 12.8 (2022): 4077.
  Butt, U. A., Amin, R., Mehmood, M., Aldabbas, H., Alharbi, M. T., & Albaqami, N. (2023). Cloud security threats and solutions: A survey. Wireless Personal Communications, 128(1), 387-413.
AI-Driven Security & Future Trends
  Ejeofobiri, Chigozie K., Olayinka Olubola Victor-Igun, and Clifford Okoye. "AI-Driven Secure Intrusion Detection for Internet of Things (IOT) Networks." Asian Journal of Mathematics and Computer Research 31.4 (2024): 40-55.
  Abdulhasan, Maki Mahdi, et al. "AI-Driven Privacy Analysis of IoT Services in Edge Computing." 2024 International Conference on Emerging Research in Computational Science (ICERCS). IEEE, 2024.
  Bast, C., & Yeh, K. H. (2024). Emerging authentication technologies for zero trust on the internet of things. Symmetry, 16(8), 993.
  Sharma, Neha, and Pankaj Dhiman. "A survey on IoT security: challenges and their solutions using machine learning and blockchain technology." Cluster Computing 28.5 (2025): 313.

## Slide 50
Questions and Discussion
?