## Slide 1
Ασφάλεια Συστημάτων & Δικτύων
Διάλεξη 07

## Slide 2
Game: Answer the questions (cycle)
Correct: +1 point for the class (aggregate)
Wrong: -1 point for the class (aggregate)
Pass: 0 points

## Slide 3
1. Which element has the chemical symbol ‘Fe’?
A) Fluorine B) Iron C) Francium

## Slide 4
1. Which element has the chemical symbol ‘Fe’?
A) Fluorine B) Iron C) Francium

## Slide 5
2. In computer networks, what does ‘IP’ stand for?
A) Internet Protocol B) Internal Processing C) Input Parameter

## Slide 6
2. In computer networks, what does ‘IP’ stand for?
A) Internet Protocol B) Internal Processing C) Input Parameter

## Slide 7
3. Who proposed the theory of general relativity?
A) Isaac Newton B) Albert Einstein C) Niels Bohr

## Slide 8
3. Who proposed the theory of general relativity?
A) Isaac Newton B) Albert Einstein C) Niels Bohr

## Slide 9
4. Which country is both in Europe and Asia?
A) Turkey B) Poland C) Egypt

## Slide 10
4. Which country is both in Europe and Asia?
A) Turkey B) Poland C) Egypt

## Slide 11
5. Who invented the World Wide Web?
A) Tim Berners-Lee B) Bill Gates C) Steve Jobs

## Slide 12
5. Who invented the World Wide Web?
A) Tim Berners-Lee B) Bill Gates C) Steve Jobs

## Slide 13
6. What is the smallest unit of life that can replicate independently?
A) Atom B) Cell C) Molecule

## Slide 14
6. What is the smallest unit of life that can replicate independently?
A) Atom B) Cell C) Molecule

## Slide 15
7. Which gas is most abundant in the Earth’s atmosphere?
A) Oxygen B) Nitrogen C) Carbon dioxide

## Slide 16
7. Which gas is most abundant in the Earth’s atmosphere?
A) Oxygen B) Nitrogen C) Carbon dioxide

## Slide 17
8. Which organ in the human body produces insulin?
A) Liver B) Pancreas C) Kidney

## Slide 18
8. Which organ in the human body produces insulin?
A) Liver B) Pancreas C) Kidney

## Slide 19
9. Which river is the longest in the world?
A) Nile B) Amazon C) Yangtze

## Slide 20
9. Which river is the longest in the world?
A) Nile B) Amazon C) Yangtze

## Slide 21
10. The Renaissance period began in which country?
A) France B) Italy C) Spain

## Slide 22
10. The Renaissance period began in which country?
A) France B) Italy C) Spain

## Slide 23
11. In which year did the Berlin Wall fall?
A) 1989 B) 1991 C) 1985

## Slide 24
11. In which year did the Berlin Wall fall?
A) 1989 B) 1991 C) 1985

## Slide 25
12. Who painted the ceiling of the Sistine Chapel?
A) Leonardo da Vinci B) Michelangelo C) Raphael

## Slide 26
12. Who painted the ceiling of the Sistine Chapel?
A) Leonardo da Vinci B) Michelangelo C) Raphael

## Slide 27
13. The famous painting “Starry Night” was created by…
A) Vincent van Gogh B) Claude Monet C) Pablo Picasso

## Slide 28
13. The famous painting “Starry Night” was created by…
A) Vincent van Gogh B) Claude Monet C) Pablo Picasso

## Slide 29
14. Which city hosted the 2016 Summer Olympics?
A) Tokyo B) Rio de Janeiro C) London

## Slide 30
14. Which city hosted the 2016 Summer Olympics?
A) Tokyo B) Rio de Janeiro C) London

## Slide 31
15. What is the main ingredient in traditional Japanese miso soup?
A) Soybeans B) Rice C) Seaweed

## Slide 32
15. What is the main ingredient in traditional Japanese miso soup?
A) Soybeans B) Rice C) Seaweed

## Slide 33
Total Points: WHO WAS THE WEAKEST LINK?

## Slide 34
Ασφάλεια στο Φυσικό Επίπεδο (Physical Layer – L1)

## Slide 35
Recap: The OSI Model
Open Systems Interconnection (OSI) Model
Developed by ISO to standardize networking communication.
Divides the process of data communication into 7 layers.
Helps in designing, understanding and troubleshooting networks.
Layer | Name | Main Function | Example
7 | Application | Provides network services to users | Web Browser / HTTP, Email / SMTP
6 | Presentation | Data formatting, encryption | TLS/SSL, JPEG / MP3
5 | Session | Manages sessions & connections | HTTPS session, Database connections
4 | Transport | Reliable or fast data delivery | TCP, UDP
3 | Network | Data routing | IP, ICMP
2 | Data Link | Data framing, MAC address handling | Ethernet, Wi-Fi
1 | Physical | Raw bit transmission | Cable, Wi-Fi

## Slide 36
Preliminaries: Physical Layer (L1) overview
Lowest layer of the OSI model
Handles physical transmission of raw bitstreams over a communication medium
Defines electrical, mechanical, optical and radio specifications
Converts (digital) bits (0/1) into (analog) signals (voltage, light pulses, RF waves)
Determines connector types, pinouts, frequencies, modulation techniques
Responsible for bit rate, signal encoding, synchronization and media access at the most fundamental level
No understanding of frames, packets, addresses, or protocols
Interfaces directly with physical hardware: cables, antennas, transceivers, NIC PHY chips
Ensures that bits are successfully placed on the medium and received without physical corruption

## Slide 37
Preliminaries: Physical Layer (L1) definition
Physical Layer Type | Description & Architecture
Copper Cabling (UTP, STP, Coaxial) | Transmits electrical signals over metal conductors; supports Ethernet standards; uses connectors (RJ45, BNC)
Fiber Optics | Uses light pulses through glass or plastic fibers; supports high bandwidth and long-distance transmission
Wireless RF (Wi-Fi, Bluetooth, Zigbee) | Uses radio frequency waves for short- to medium-range communication; requires antennas, transceivers, and channel allocation.
Cellular (4G, 5G) | Uses licensed spectrum with base stations (eNodeB/gNodeB) communicating with mobile devices; supports wide-area coverage and mobility.
Satellite Links | Long-distance communication via geostationary or low-earth-orbit satellites; uses RF transmission and ground station antennas.
Infrared (IR) | Uses line-of-sight infrared light for short-range, point-to-point communication; common in remotes and sensors.
NFC / RFID | Short-range communication using inductive coupling between reader and tag; used for identification, payments, and access control.
Definition: The Physical Layer (L1) is the lowest layer of the OSI and TCP/IP models that defines how raw bits are transmitted as electrical, optical, or radio signals over physical media. It specifies hardware interfaces, modulation, signal strength, cabling and the physical characteristics enabling communication between devices.

## Slide 38
Physical Layer Security: Motivation
Communication starts at the PHY medium
  Wire
  Fiber
  Air
Higher-layer security depends on reliable L1 operation
  If L1 fails -> higher-layer protections cannot function
L1 is the foundation of the trusted computing base
Misconfigurations or vulnerabilities “below the protocol stack” cannot be mitigated above it

## Slide 39
Physical Layer Security: Impact
Physical disruptions cause
  service outages
  data loss
  network unavailability
Accidental damage dominates real-world incidents
  Construction cuts
  Power issues
Wireless is a shared medium
  Inherently exposed to interference and misuse
Physical infrastructure cost
  Expensive to deploy and costly to repair
Physical access often bypasses logical controls

## Slide 40
Physical Layer Security: Major Incidents
Year | L1 Type | Incident | Impact / Consequence
1990s - 2000s | Military Jamming (R-330Zh “Zhitel”) | Russian systems used to interfere with GPS, satellite communications and mobile phones. | Denial of navigation and communications to adversary systems; used in conflict zones.
2000s | Electronic Warfare (EW) Jamming (Krasukha System) | Deployment of electronic warfare jammers to deny GPS to drones and aircraft. | Loss of GPS for drones; some drones reportedly lost control or crashed.
2008 | Undersea Fiber Cable | Submarine cables severed in the Mediterranean (anchor / dragging ship). | Internet and phone disruptions: up to 70% capacity loss; millions of users affected.
2013 | Undersea Fiber Cable | Attempted sabotage of Sea-Me-We-4 submarine cable in Egypt. | Potential 50% disruption of Egypt’s international Internet capacity.
2022 | GPS/GNSS (Aviation) | RAF aircraft carrying UK Defence Secretary experienced GPS jamming near Kaliningrad. | 30 minutes loss of GPS navigation; alternative navigation required.
2024 | Undersea Fiber Cable | Baltic Sea cables damaged; suspected sabotage. | Regional telecom disruption; some services slowed or rerouted; geopolitical concern.
2024 | Undersea Power + Telecom Cable | Estlink‑2 and telecom cables ruptured (anchor dragging suspected). | Cross-border power capacity reduced; repair costs tens of millions of euros.
2024 | GPS/GNSS (Commercial Aviation) | Finnair suspended flights to Tartu, Estonia after GPS interference prevented landing. | Flights diverted or canceled; safety risk in GPS‑dependent approaches.
2025 | GPS/GNSS (Military) | GPS jamming near Kaliningrad affecting drones. | Commercial and professional drones experienced signal loss or crash; navigation disrupted.

## Slide 41
Common Physical Layer Attack Categories
L1
Interception
Interference
Manipulation
Disruption
Environmental
Converting or capturing physical signals (electrical, optical, RF)
Disrupting or degrading the signal (noise, obstruction, interference sources)
Altering the medium or signal (tampering, unauthorized connectors, rogue devices)
Cutting, disconnecting, powering down, or overwhelming physical channels
Heat, vibration, electromagnetic effects, improper shielding, equipment aging

## Slide 42
L1 Security & CIA Triad
Signal isolation
Shielding
Redundant Links
Physical Protection (racks)
Directional Antennas
Certified Cabling
Diverse Routing
Spectrum Management
Secure channels
Error Detection (PHY)
UPS
Electromagnetic compatibility

## Slide 43
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Mitigation

## Slide 44
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Mitigation

## Slide 45
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Physical access zones, equipment rooms, wiring closets, roof-mounted antennas, publicly accessible wireless areas
Mitigation

## Slide 46
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Physical access zones, equipment rooms, wiring closets, roof-mounted antennas, publicly accessible wireless areas
Disrupt communication, intercept signals, manipulate transmissions, degrade quality, cause outages
Mitigation

## Slide 47
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Physical access zones, equipment rooms, wiring closets, roof-mounted antennas, publicly accessible wireless areas
Disrupt communication, intercept signals, manipulate transmissions, degrade quality, cause outages
Physical tampering, environmental stresses, miswired or damaged cable, interference sources, unauthorized RF devices
Mitigation

## Slide 48
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Physical access zones, equipment rooms, wiring closets, roof-mounted antennas, publicly accessible wireless areas
Disrupt communication, intercept signals, manipulate transmissions, degrade quality, cause outages
Physical tampering, environmental stresses, miswired or damaged cable, interference sources, unauthorized RF devices
Outages, degraded performance, loss of service continuity, incorrect signal transmission
Mitigation

## Slide 49
L1 Threat Modelling
Assets
Trust Boundaries
Attackers & Goals
Attack Vectors
Risks
Physical Layer (L1)
Media (copper, fiber), antennas, transceivers, cabling, patch panels, power systems, physical infrastructure
Physical access zones, equipment rooms, wiring closets, roof-mounted antennas, publicly accessible wireless areas
Disrupt communication, intercept signals, manipulate transmissions, degrade quality, cause outages
Physical tampering, environmental stresses, miswired or damaged cable, interference sources, unauthorized RF devices
Outages, degraded performance, loss of service continuity, incorrect signal transmission
Mitigation
Controlled physical access, robust cabling & installation standards, environmental monitoring, redundancy, spectrum planning & RF surveys

## Slide 50
L1 Security Taxonomy
Wired Medium
L1 Security
Wireless Medium
Copper (Coaxial, Ethernet)
Fiber Optics
Power Lines
Serial Links (CAN)
Backplane (electrical connectors, bus)
Wi-Fi (802.11)
Cellular (2G, 3G, 4G/LTE, 5G)
Bluetooth/BLE
RFID/NFC
IoT (ZigBee, LoRaWAN, SigFox, Z-Wave)
GPS/GNSS
Satellite communications
Microwave links for point-to-point

## Slide 51
Wired L1 Security: Copper - Overview
Definition
  Twisted-pair or coaxial cabling that carries electrical signals for communications
Common forms
  UTP (Cat5e/6/6A)
  STP/FTP
  coax (RG-6/59)
  Legacy Ethernet over coax
  DSL copper pairs
Typical uses
  Campus/building Ethernet
  Access wiring to switches
  CCTV coax feeds
  Last-mile copper
UTP
STP
Coaxial

## Slide 52
Wired L1 Security: Copper – Threats & Vulnerabilities
Electromagnetic leakage (EME)
  Unshielded pairs emit signals that can be picked up remotely (TEMPEST concept).
Inductive/capacitive tapping (non-invasive)
  Clamps or probes near a cable can recover signal without cutting.
Connector & patch-panel tampering
  Exposed jacks or patch-panels enable insertion of rogue devices (Man-in-the-Middle - MITM attacks).
Physical cuts & damage
  Accidental excavation or deliberate cutting causes immediate outage.
Interference & crosstalk
  Nearby power lines or poor routing cause attenuation and errors.
Aging/poor termination
  Degraded performance from bad crimps, water ingress, or runs beyond spec

## Slide 53
Wired L1 Security: Copper – Mitigations
Physical hardening
  Locked telecom rooms
  Tamper-evident patch panels
  Secured conduits and risers.
Shielding & cable choice
  STP/FTP or shielded coax where EM protection needed
  Proper grounding.
Routing & separation
  Distance from power runs
  Dedicated conduits for critical links.
Access & change management
  Inventory ports
  Disable unused jacks
  Documented patching procedures.
Testing & monitoring tools
  Cable certifiers (pair integrity, length, wiremap)
  Periodic physical inspections.
Redundancy & diversity
  Alternate paths
  Diverse conduits
  Reduce single-point failures.

## Slide 54
Wired L1 Security: Fiber Optics - Overview
Definition
  Transmission of data as light pulses through glass or plastic optical fibers.
Common types
  Single-mode (long-haul)
  Multi-mode (campus/metro)
  Connector types (LC, SC, ST).
Typical uses
  Backbone links
  Long-distance aggregation
  Data-center interconnects

## Slide 55
Wired L1 Security: Fiber Optics – Threats & Vulnerabilities
Physical cuts & breaks
  Cable damage from anchors, construction, or abrasion causes outages.
Micro/macro-bending taps
  Deliberate bends or microbends can leak light for interception (requires physical access).
Splice/splitter compromise
  Inserting splitters or tampering splice enclosures can duplicate signals.
Connector/patch substitution
  Replacing a patch/jumper with a compromised splitter or tapped jumper.
Attenuation & degradation
  Dirty connectors, poor splices, or moisture increase loss and reduce link margin.
Fiber aging & mechanical stress
  Repeated flexing or improper bend radius causes progressive failure.

## Slide 56
Wired L1 Security: Fiber Optics – Mitigations
Physical protection
  Locked manholes
  Armored cable
  Sealed conduits.
OTDR (Optical Time-Domain Reflectometer) monitoring
  Continuous or scheduled OTDR traces
  Detect bends, splices, cut locations and sudden loss
Power/spectrum monitoring
  Inline optical power meters
  Alarm thresholds
  Detect unexpected loss
Inventory & tamper evidence
  Documented fiber routes
  Photographed splice records
Diversity & resilience:
  Route diversity (different ducts/paths)
  Spare wavelength capacity
Operational hygiene
  Clean connectors
  Correct bend radius
  Qualified splicing procedures and audits.

## Slide 57
Wireless L1 Security: Basic Concepts
Radio Frequency (RF): data transmitted as electromagnetic waves in air
Spectrum & Bands: licensed (cellular), unlicensed (Wi-Fi/Bluetooth 2.4/5/6 GHz)
Channels: frequency slices used to separate simultaneous transmissions
Antennas: Omnidirectional for wide area coverage, Directional/High-gain for long-distance focusing
Propagation: attenuation, reflection, multipath, interference, noise
Modulation: how data is encoded onto a carrier
Coverage & Range: affected by power, frequency, antenna gain, obstacles

## Slide 58
Wireless L1 Security: WiFi - Overview
Uses unlicensed bands
  2.4 / 5 / 6 GHz
Common protocols
  802.11 a/b/g/n/ac/ax.
Devices connect through access points (APs) using RF channels.
Used for
  Home & enterprise networks
  Public hotspots
  IoT connectivity.

## Slide 59
Wireless L1 Security: WiFi - Threats & Vulnerabilities
Eavesdropping
  Signals broadcast
  Can be received by anyone in range.
Interference/Jamming
  Intentional or accidental RF noise disrupts service.
Unauthorized APs (Rogue/Evil Twin)
  Spoofing SSID/BSSID to attract clients.
Deauth/Disassoc manipulation
  Unprotected management frames in older standards.
Range extension attacks
  High-gain antennas enable long-distance sniffing.
RF leakage through walls/windows
  Wireless escapes physical boundaries.

## Slide 60
Wireless L1 Security: WiFi - Mitigations
Physical controls
  AP placement
  Directional antennas
  Signal containment.
Use modern standards
  WPA3
  Protected management frames (802.11w).
Spectrum monitoring
  Kismet
  Wi-Fi IDS/WIPS for rogue AP detection.
Channel planning
  Reduce interference
  Avoid congested bands.
RF hygiene
  Proper power settings
  Shielding in sensitive environments.
Site surveys
  Measure coverage
  Dead zones
  Leakage areas.

## Slide 61
Wireless L1 Security: Cellular (B5G) - Overview
Operate in licensed spectrum, tightly regulated
Components
  User Equipment (UE)
  Base Stations (eNodeB/gNodeB)
  Core Network.
Technologies
  LTE (4G)
  5G NR
Used for:
  Wide-area coverage
  Mobility
  IoT (NB-IoT)
  Emergency communications

## Slide 62
Wireless L1 Security: Cellular - Threats & Vulnerabilities
IMSI catchers (stingrays): fake base stations forcing devices to connect.
Jamming/Blocking: RF interference disrupting mobile signals.
Downgrade risks: forcing devices to fall back to insecure modes (2G).
Rogue small cells: malicious microcells deployed in public areas.
Weak physical protection: remote base stations & rooftop antennas exposed.
Cross-border interference: overlapping networks near national borders.

## Slide 63
Wireless L1 Security: Cellular - Mitigations
Licensed spectrum enforcement
  Prevent arbitrary transmitter deployment
Base station hardening
  Physical locks
  Surveillance
  Tamper-evident seals.
RF monitoring
  Spectrum analyzers
  Detect rogue cells & unusual signals.
Network configuration
  Disabling legacy 2G fallback
  Secure handover policies.
MNO (Mobile Network Operator) controls
  SIM authentication
  Key rotation
  Mobility management.
Coverage audits
  Measure signal quality
  Detect anomalies in power or cell IDs.

## Slide 64
Wireless L1 Security: Satellite Communications - Overview
Uses RF links between
  Ground stations
  User terminals
  Satellites.
Types:
  GEO (Geostationary Earth Orbit)
  MEO (Medium Earth Orbit)
  LEO (Low Earth Orbit)
Applications
  Maritime/aviation Internet
  Remote areas,
  Military
  Broadcasting.

## Slide 65
Wireless L1 Security: SatComms - Threats & Vulnerabilities
Long-range eavesdropping
  Wide-area beams can be intercepted far away
Uplink jamming
  Attackers disrupt communication between ground and satellite.
Downlink interference
  Noise injected into broad satellite footprints.
Terminal hijacking
  Poorly secured ground terminals manipulated physically.
Physical threats to ground stations:
  Antennas
  Dish alignment
  Cable access.
Orbital path issues
  Solar weather
  Signal fading
  Atmospheric loss.

## Slide 66
Wireless L1 Security: SatComms - Mitigations
Directional antennas
  Narrow beams reduce interception footprint
Link budgets & monitoring
  Detect unexpected power anomalies.
Ground station hardening
  Fences
  CCTV
  Anti-tamper cases
  Alignment locks
Spectrum monitoring
  Detect uplink/downlink interference
  Detect spoofing.
Redundancy
  Multiple satellites/routes
  Fallback comms.
Operational hygiene
  Secure terminals
  Firmware maintenance
  Access control

## Slide 67
Group Exercise
Harder to Defend:
The Cable or the Air?

## Slide 68
Group Exercise
No walls, no pipes … signals travel through open air.
Everyone can listen … any device in range is a potential eavesdropper.
No physical access needed … attackers don’t touch cables or equipment.
Easy to jam or disrupt … low-power interference can take down links.
Invisible adversaries … attacks leave little to no trace.
PHY & MAC exposed … management frames and RF signals can be exploited.
High-gain antennas extend the attack surface … attackers can operate from far away.
No Wires, No Walls
Wireless Is Inherently Insecure

## Slide 69
A Deep Dive into Wireless L1 Security
  Wireless has no physical boundary
    Anyone in range can listen, inject, or jam
  Relies on radio waves that propagate freely
  Inherently exposed – higher layers thus need:
    strong cryptography
    protocol security
  Focus on Wi-Fi (802.11)
    Widely used wireless technology
    Homes, enterprises, universities
    Highest attack surface
  Understanding Wi-Fi security = real-world wireless risk

## Slide 70
Wi-Fi L1 Security: Overview
Key Technical Terms
  802.11 — IEEE standard defining how Wi-Fi communicates over the air
  SSID — Network name broadcast by an access point
  AP (Access Point) — Device that provides Wi-Fi connectivity
  Client/Station (STA)— Wireless station (laptop, phone, IoT device)
  WPA (Wi-Fi Protected Access) — Family of standards securing Wi-Fi connections
    WEP/WPA/WPA2/WPA3 — Generations of Wi-Fi security protocols
  PSK (Pre-Shared Key) — Shared password mode for home Wi-Fi
  802.1X/EAP(Extensible Authentication Protocol) — Enterprise authentication framework using credentials/certificates
  Modern encryption/integrity algorithms used in Wi-Fi
    AES-CCMP(Advanced Encryption Standard - Cipher Block Chaining Message)
    AES-GCMP(Advanced Encryption Standard - Cipher Galois Message Authentication Code
  PMF (Protected Management Frames) — Protects deauth/disassoc messages
  SAE (Simultaneous Authentication of Equals) — WPA3’s secure handshake with forward secrecy
Wi-Fi Security High-Level Functionality
  Authenticates users/devices
  Establishes encrypted communication keys
  Protects confidentiality & integrity of wireless frames
  Compensates for the insecure physical medium (open air)

## Slide 71
Evolution of Wi-Fi Security: The Big Picture
WEP
First attempt at wireless security
Weak crypto (RC4)
Quickly broken
WPA
Transitional upgrade
Still RC4-based
Improved integrity
PSKey issues remain
WPA2
Real security standard
AES-CCMP
Modern key management
Basis of all enterprise Wi-Fi today
WPA3
Fixes PSK problems with SAE
Mandatory management frame protection
Better crypto
Forward secrecy

## Slide 72
The 4 Pillars of Modern Wi-Fi Security
Authentication
Who joins the network?
SAE (Simultaneous Authentication of Equals)
Replaces PSK
Resists offline dictionary attacks
Provides mutual authentication with forward secrecy
2) Key Management
How session keys are created?
4-Way Handshake (WPA2/WPA3 architecture)
Derives per-session keys
Protects against replay & tampering via message integrity
3) Data Protection
How frames are protected
AES-CCMP (WPA2)
AES-GCMP (WPA3; faster & stronger)
Ensures confidentiality
Ensures integrity of every frame
4) Management Frame Protection
Protecting the control plane
PMF/802.11w mandatory in WPA3
Prevents deauth/disassoc spoofing
Secures Wi-Fi’s “control traffic”

## Slide 73
Modern Wi-Fi Security Flow: Overview
Discovery (L1/MAC)
Authentication (Higher Layer)
Key Exchange (MAC Layer)
Protected Data Phase (Link Layer)
Session Maintenance
Note: WPA3 builds three layers of protection (authentication, key management and encryption) directly on top of an untrusted physical medium.

## Slide 74
Modern Wi-Fi Security Flow: 1 - Discovery & Initial Contact (L1/MAC level)
Passive discovery
  APs periodically send Beacon frames (SSID, supported rates, capabilities, WPA3 info).
  Clients listen (monitor mode) and learn available networks.
Active discovery
  Client sends Probe Request to query SSIDs or broadcast probe.
  AP replies with Probe Response
Association
  Client sends Association Request (capabilities, listen interval).
  AP replies Association Response
  Logical link established (MAC-level association).
Where security info appears
  Announcement of WPA/WPA2/WPA3 support
  Announcement of cipher suites (e.g., AES-GCMP).
Why this step matters
  Sets the stage for secure negotiation
  At this stage nothing is confidential
  Beacons are public
  Establishes the MAC-level conversation over an untrusted L1.
  Discovery happens on the air (fully exposed).
  Security begins after association via cryptographic handshakes.

## Slide 75
Modern Wi-Fi Security Flow: 2 - Authentication: SAE and 802.1X/EAP
SAE (Simultaneous Authentication of Equals) for General Usage:
  Two devices auth each other simultaneously
  Password is not exposed during handshake
  Provides resistance to offline dictionary attacks.
  Offers forward secrecy (past sessions safe even if password leaks later)
802.1X/EAP for Enterprise:
  Network authentication via an Authentication Server (RADIUS)
  Client ↔ AP ↔ RADIUS flow results in derived master key (MSK/PMK).
  Supports certificate-based auth (stronger than passwords).
Message-level
  SAE: commit/confirm messages exchanged between STA ↔ AP (over MAC).
  802.1X/EAP: EAP-Request/Response, then RADIUS exchange to derive PMK.
Why authentication matters
  Confirms identities before keys are derived
  Prevents impersonation.
L1 connection
  Authentication runs over insecure RF
  Cryptographic SAE and protected EAP flows ensure:
    adversary listening on L1 cannot trivially obtain secrets.

## Slide 76
Modern Wi-Fi Security Flow: 3 - Key Derivation and 4-Way Handshake
Primary keys & roles
  PMK (Pairwise Master Key)
    root secret
    derived from SAE/EAP.
  PTK (Pairwise Transient Key)
    per-client key used to encrypt unicast data
    derived from PMK + NumberUsedOnce (Nonce) + MACs.
  GTK (Group Temporal Key)
    used to encrypt multicast/broadcast frames
    shared by all STAs
4-Way Handshake (purpose & flow)
  Goal: derive PTK and confirm both parties hold the PMK.
  Steps:
    AP -> STA: ANonce (AP nonce)
    STA -> AP: SNonce + MIC (includes STA’s capabilities)
    AP -> STA: Install PTK + GTK + MIC
    STA -> AP: Install PTK confirmation (ACK)
  Uses Nonce values, MAC addresses and a KDF (Key Derivation Function)
  to generate PTK.
Replay & integrity protections
  Each handshake message includes Message Integrity Codes (MICs)
  Also sequence counters to prevent replay/injection.
Why this matters
  Keys are unique per-session/per-client.
  Avoids reusing long-term secrets for frame encryption
  Limits exposure if keys leak.
L1 connection: The 4-way handshake runs over untrusted air. Nonces and MICs are used so an eavesdropper cannot derive session keys from passive capture even though they see the handshake messages.

## Slide 77
Modern Wi-Fi Security Flow: 4 - Data Protection (Encrypting & Authenticating Frames)
Encryption algorithms
  AES-CCMP (CCM-based) for WPA2
  AES-GCMP (Galois/Counter Mode) for WPA3
What is protected
  Data payloads of unicast frames are encrypted with PTK-derived keys.
  Broadcast/multicast frames use GTK.
  Management frames are protected by PMF (if enabled)
AEAD (Authenticated Encryption with Associated Data)
  Encrypt and authenticate in one primitive
  Sequence numbers and replay counters prevent replayed frames from being accepted.
Key lifecycle
  Per-session keys have limited lifetimes
Why this matters
  Encrypted frames prevent an eavesdropping
  Prevent modification/injection
L1 connection
  Data encryption masks the content transmitted over L1
  Integrity/authentication makes injected raw RF frames detectable and discardable

## Slide 78
Modern Wi-Fi Security Flow: 5 - Session Maintenance, Roaming & Rekeying
Rekeying & GTK updates
  AP periodically rotates the GTK (multicast)
  Can force PTK rekey and fresh nonce exchange
  Limits the amount of data encrypted under a single key
Roaming & fast handoff
  802.11r (Fast BSS Transition)
    Enables faster roaming between APs
  PMK Caching/802.11r/802.11k/v
    Mechanisms to preserve security while enabling seamless mobility.
PMF & session resilience
  PMF prevents deauth/disassoc spoofing used to force reauth cycles.
  In WPA3, PMF is mandatory
  Improves session resilience against L1-based attacks on the control plane.
Session expiration & re-authentication
  Long-lived sessions should enforce periodic re-auth
  Certificate rotation (enterprise) to limit exposure.
Why this matters
  Security must survive client movement and long-lived sessions
  Rekeying and roaming protocols ensure continuity without weakening cryptography.
L1 connection
  Mobility and transient RF conditions increase opportunities for interception or session hijack
  Robust rekeying and fast secure handoffs reduce window of exposure on the open air.

## Slide 79
Wi-Fi L1 Threats
L1 Threat | High-Level Description (PHY/MAC-level) | Real-World Example
RF Eavesdropping | Receiving frames from the air without physical access; (encryption is weak/misconfigured) | Airport/café Wi-Fi sniffing demonstrations; KRACK also re-enabled partial passive recovery.
Jamming/RF DoS | Flooding the channel (noise, continuous carriers, high-power transmissions) to block Wi-Fi communication. | Sports arena & conference jamming incidents caused by wireless microphones/cameras.
Deauthentication - Disassociation Frames | Spoofed management frames kick clients off APs. Pure MAC-layer (no encryption pre-PMF). | Marriott 2014 deauth controversy
Rogue High-Gain Antenna Interception | Long-range directional antennas capture Wi-Fi traffic from far outside expected perimeter. | Wardriving/war-sitting setups that captured enterprise Wi-Fi from adjacent buildings.
Replay of Management/Control Frames | Reinjecting captured unprotected frames (e.g., beacons, probes, some Mgmt frames pre-802.11w). | Red-team exercises replaying beacons/probes to trick wireless IDS sensors.
Signal Spoofing/Fake Beacons | Broadcasting crafted beacon frames to mislead clients about SSIDs, capabilities, or channel environment. | Large conferences where rogue beacon floods caused Wi-Fi instability.
Channel Saturation/CSMA Abuse | Occupying airtime with frequent low-rate frames or backoff manipulation to cause unfair channel use. | “Sticky client” attacks and low-rate broadcast floods observed in university Wi-Fi outages.
Physical Radio Interference (Non-Malicious) | Microwave ovens, Bluetooth, IoT RF noise disrupting 2.4 GHz channels. | University Wi-Fi collapse tied to old microwave ovens radiating into channel 6.

## Slide 80
Wi-Fi L1 Mitigations
Defense Mechanism | High-Level Purpose (L1/MAC Focus) | What It Mitigates
AP Placement & Antenna Patterns | Directional antennas, proper height, controlled coverage footprint | Long-range interception, rogue antenna eavesdropping.
RF Shielding & Physical Barriers | Walls, filters, Faraday paint/film to contain or attenuate RF. | Eavesdropping, unauthorized signal leakage.
5 GHz/6 GHz Adoption | Higher frequencies = shorter range, less wall penetration; reduces exposure surface. | External sniffing, long-range interception.
802.11w PMF (Protected Management Frames) | Encrypts/de-auth protects mgmt frames at MAC layer. | Deauth/disassoc attacks, spoofed control frames.
WPA3/SAE Mandatory | Strong handshake with resistance to offline guessing; modern crypto baseline. | Weak encryption allowing passive capture.
Channel Planning & Interference Management | Proper channel selection, power tuning | Jamming susceptibility, channel saturation.
Wireless IPS/IDS | Monitors RF for rogue APs, spoofed beacons, jamming patterns. | Rogue APs, fake beacons, interference anomalies.
Regular Site Surveys (Active/Passive) | Measure coverage, detect bleed, verify channels & rogue signals. | RF leak paths, rogue transmitters, misconfigurations.

## Slide 81
Quick Demo
Using your phone Wi-Fi scanner (built-in or apps like WiFi Analyzer):
  Observe SSID list and BSSIDs
  Note signal strength (RSSI)
  Identify encryption types (WPA2/WPA3/Open)
  Look for rogue or unusual Aps
Cross-check with Netspot

## Slide 82
Group Question
Which network is safer at L1: a fully wired campus network or a fully Wi-Fi campus network (assuming both are professionally managed)?

## Slide 83
Group Question
Aspect | Wired (Copper/Fiber) | Wireless (Wi-Fi/5G/Satellite) | Winner
Physical Security | Hard to intercept remotely, requires physical access | Signal propagates freely, anyone in range can receive it | Wired
Vulnerabilities | Exposed cable runs, patch panels, human tampering, fiber splice compromise | Eavesdropping, jamming, rogue APs, deauth/disassoc, high-gain interception | Wired
Availability Risk | Single cable/fiber cut can disrupt connectivity | Easy to disrupt via RF interference or targeted attacks | Tie (Context-dependent)
Ease of Monitoring | High: OTDR, cable certifiers, physical inspections | Moderate: RF monitoring, spectrum analysis, WIPS | Wired
Overall L1 Risk | Moderate: generally safe unless physical access is possible | High: inherently insecure due to broadcast nature | Wired
Key Takeaways:
Wireless is inherently more exposed at Layer 1
Wired networks are generally safer unless physical access is compromised.

## Slide 84
References
On L1 security (generic)
  Lv, Lu, et al. "Safeguarding next-generation multiple access using physical layer security techniques: A tutorial." Proceedings of the IEEE (2024).
  Duan, Zhuoying, et al. "Adaptive Strategies in Enhancing Physical Layer Security: A Comprehensive Survey." ACM Computing Surveys 57.7 (2025): 1-36.
Wired L1 security
  Mao, Xiaoxin, et al. "100-Gbit/s 100-km physical-layer secure fiber-optic communication using wideband chaotic semiconductor lasers." Journal of Lightwave Technology (2024).
  Sadot, Dan, et al. "Physical layer security in high-speed optical communications." Journal of Lightwave Technology (2024).
  Fernandez, Javier Hernandez, Roberto Di Pietro, and Javier/Omri Hernandez Fernandez (Ayme). Physical Layer Security in Power Line Communications. 2024.
Wireless L1 security
  Harvanek, Michal, et al. "Survey on 5G physical layer security threats and countermeasures." Sensors (Basel, Switzerland) 24.17 (2024): 5523.
  Devi, Parmila, Manoranjan Rai Bharti, and Dikshant Gautam. "A survey on physical layer security for 5G/6G communications over different fading channels: Approaches, challenges, and future directions." Vehicular Communications (2025): 100891.
  Lo Cigno, Renato, et al. "Communication and Sensing: Wireless PHY-Layer Threats to Security and Privacy for IoT Systems and Possible Countermeasures." Information 16.1 (2025): 1-18.
  Abdelsalam, Nora, Saif Al‐Kuwari, and Aiman Erbad. "Physical layer security in satellite communication: State‐of‐the‐art and open problems." IET Communications 19.1 (2025): e12830.
Wi-Fi related
  Afzal, Faiza, et al. "An Enhanced Approach for Wi-Fi Security and Authentication Protocols: A Systematic Approach towards WEP, WPA, WPA2, and WPA3." Spectrum of Engineering Sciences 2.5 (2024): 379-403.
  Zhang, Yuanyuan, et al. "Enhancing Physical Layer Authentication in Mobile WiFi Environments Using Sliding Window and Deep Learning." IEEE Transactions on Wireless Communications (2024).
Monitoring & Tools
  Abdalla, Aly S., Bo Tang, and Vuk Marojevic. "AI at the Physical Layer for Wireless Network Security and Privacy." Artificial Intelligence for Future Networks (2025): 341-380.
  Kismet: https://www.kismetwireless.net/
  Amoo, Olukunle Oladipupo, et al. "Cybersecurity threats in the age of IoT: A review of protective measures." International Journal of Science and Research Archive 11.1 (2024): 1304-1310.

## Slide 85
Questions and Discussion
?